# IUPAC Task Group on Atmospheric chemical Kinetic Data Evaluation – Data Sheet VI.A4.28 HET_SL_28

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac-pole-ether.fr.

This data sheet last evaluated: June 2011; last change in preferred values: June 2011.

BrONO2 + H2SO4 (aq) → products

Experimental data

| Parameter | H2SO4 / wt% | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- | --- |
| Uptake coefficients:  |  |  |  |  |
| 0.5(+0.5, -0.25) 0.4(+0.6, -0.2) 0.3(+0.7, -0.1) | 45 60 70 | 210 210 220 | Hanson and Ravishankara, 1995 | CWFT-CIMS (a) |
| 1.0 (0.1 m radius) 0.81 (0.1 m radius) 0.75 (0.1 m radius) 0.26 (0.1 m radius) | 48 47 66 76.5 | 229 249 272 294 | Hanson et al., 1996 | AFT-CIMS (b) |
| 0.8 | 66 | 250 | Hanson, 2003 | RWFT and AFT-CIMS (c) |
| 0.95 | 72 | 250 |  |  |
| 0.5 | 75 | 250-293 |  |  |
| 0.2 | 79 | 250-293 |  |  |
| 0.15 | 82 | 250-293 |  |  |

Comments

(a)	Uptake measurement on a wetted wall flow tube coupled to CIMS detection.  The source ion was SF6- and BrONO2 and HOBr were monitored as BrONO2•F- and SF5O-, respectively. Large corrections (factor 5) to the observed loss rates of BrONO2 were made to take diffusive effects into account.  HOBr was detected as the primary hydrolysis product of the title reaction at a typical partial pressure of BrONO2 of (1-3) x 107 molecule cm-3.

(b)	Aerosol flow reactor operated at total pressures (N2) ranging from 239 ± 40 (majority of experiments) to 825 ± 13 mbar between 249 and 298K.  BrONO2 (1012 molecule cm-3), HOBr and HNO3 were detected as BrONO2•F-, SF5O- and NO3-, respectively, using SF6- as reagent ion.  The sulfuric acid aerosol particle size distribution was log-normal with a typical surface area-weighted peak radius of 0.1m. Uptake coefficients  were independent of the particle radius over a range of 0.05 to 0.17 m for 78% wt H2SO4 particles at 298K. In some experiments, HCl was added to the H2SO4 in order to trap HOBr (as BrCl) in order to prevent potential regeneration of BrONO2 from reaction of HNO3 with HOBr.

(c)	Rotating CWFT with stirring of the H2SO4 film (58 – 85 wt. %, 240 - 293 K) at 0.5 – 2.6 mbar total pressure. The aerosol flow tube was operated at room temperature and 160 Torr total pressure. Initial BrONO2 concentration was 1011-1012 cm-3 in the RWFT and 1012-1013 cm-3 in the AFT. Uptake coefficients showed a strong fall off towards high H2SO4 wt%, a few representative values are listed in the table.

Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| b b | 0.8 0.11 + exp(29.2 -0.40 wt) | 210 - 300 210 – 230 |

Reliability

| log(b) log() |  0.10 ± 0.15 | 210 - 300 210 - 300 |
| --- | --- | --- |

Comments on Preferred Values

The three studies yield consistent results, with values of  close to unity in diluted (45 wt. %)   H2SO4, and decreasing to 0.15 at ~80 wt. %. Owing to the large rate constant for BrONO2 hydrolysis in the condensed phase (the authors estimate a diffusion-limited rate constant kII on the order of 109 M-1 s-1) no size-dependence of  is expected, because the reacto-diffusive length, (Dl/kII)0.5 is short.  HOBr (and HNO3) is seen as the major product of BrONO2 uptake to H2SO4. Some Br2 was also observed, which likely stems from reactions of HOBr and not from an additional BrONO2 loss process.

Since the BrONO2 solubility is not known, a detailed parameterisation of the uptake coefficient is not possible. We therefore adopt the expression suggested by Hanson (2003) that reproduces the uptake coefficients measured on both bulk and aerosol from all three studies:

References

Hanson, D.R., Ravishankara, A.R.: Geophys. Res. Lett. 22, 385-388, 1995.

Hanson, D.R., Ravishankara, A.R., Lovejoy, E.R.: J. Geophys. Res. 101, 9063-9069, 1996.

Hanson, D. R.: J. Geophys. Res., 108, art.no. 4239, doi:10.1029/2002JD002519, 2003.