### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet V.A1.18 HI18

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: March 2010; last change to preferred values: March 2010.

CH3CHO + ice

# Experimental data

| Parameter | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| , 0 |  |  |  |
| 0 > 0.1 | 120-145 | Hudson et al., 2002 | Knudsen (a) |
| 0 > 0.04 | 150 |  |  |
| 0 > 0.01 | 155 |  |  |
| 0 > 5x10-3 | 160 |  |  |
| KlinC (cm) |  |  |  |
| 3.8 x 10-10 exp(4174/T) | 140-170 | Hudson et al., 2002 | Knudsen (c) |
| 2.08  0.19 | 203 | Petitjean et al., 2009 | CWFT-MS (b) |
| 0.95  0.09 | 213 |  |  |
| 0.46  0.04 | 223 |  |  |

# Comments

(a)	Vapour deposited ice film of geometric area  5 cm2. 0 values taken from a Figure. The geometric surface area of the vapour deposited ice film was used to calculate the uptake coefficient, 0, which is a lower limit as, especially at the higher temperatures, adsorption and desorption were not separated in time.

(b)	Ice film (40-100 m thick) made from freezing liquid water at 263 K. Adsorption isotherms were measured with CH3CHO concentrations between 5.7  1011 and 8.35  1014 molecule cm-3. The data analysed using full Langmuir isotherms and the linear dependence of surface coverage on concentration to derive the partition coefficients listed in the table.

(c)	Equilibrium uptake of  4  10-7 mbar acetaldehyde ( 1010 molecule cm-3) to ice at various temperatures was analysed using the Langmuir isotherm. The expression for KlinC uses the reported value of Sads (via Trouton's rule) = -87.9 Jmol-1 K-1 and Hads = -34.7 kJmol-1 and is derived from KLangP (atm-1)  =  exp{-(T* 87.9 - 34700) / 8.314*T} using Nmax = 4  1014 molecules cm-2.

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| KlinC / cm | 7.0 x 10-8 exp(3500/T) | 203-223 |
| Nmax / molecule cm-2 | 1.3  1014 |  |

Reliability

| (E/R) | ± 300 | 203-223 |
| --- | --- | --- |
| logNmax | 0.15 |  |

##### Comments on Preferred Values

Petitjean et al. (2009) found the uptake of CH3CHO to ice surfaces to be completely reversible. They report partition coefficients and also derive an  adsorption enthalpy of –16 ( 3) kJ mol-1 by an unconstrained Van’t Hoff-type analysis of data at 203, 213 and 223 K only. In a second approach the analysis was constrained with adsorption entropy of –87.3 to derive an adsorption enthalpy of –42 kJ mol-1. The preferred values for KlinC above were obtained by fitting to the data of Petitjean et al. (2009) obtained in the linear coverage regime between 203 and 223 K. The adsorption enthalpy is ~ -29 kJ mol-1. Hudson et al. (2002) found that the interaction of CH3CHO with ice was too weak to detect close to atmospherically relevant temperatures. Extrapolation of their data to the temperatures covered by Petitjean et al. (2009) results in discrepancies of a factor of 5-10. The value of Nmax given was that obtained by Petitjean et al. (2009).

Petitjean also found the uptake of CH3CHO to ice surfaces that contained HNO3 was enhanced by 1-2 orders of magnitude at their temperatures, presumable due to dissolution in super-cooled HNO3 / H2O mixtures.  In contrast, Hudson et al. (2002) observed no uptake of CH3CHO on super-cooled HNO3 / H2O surfaces at 200 K.

# References

Hudson, P. K., Zondlo, M. A. and Tolbert, M. A.: J. Phys. Chem. A 106, 2882-2888, 2002.

Petitjean, M., Mirabel, Ph. and Le Calvé, S.: J. Phys. Chem. A 113, 5091-5098, 2009.