IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet VI.A1.14 HET_H2OL_14

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

This data sheet evaluated: 15th January 2009; last change in preferred values: 15th January 2009.

ClNO + H2O(l) H+ + Cl- + HONO

# Experimental data

| Parameter | [X]/ M | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- | --- |
| Uptake coefficients: ,ss,0 |  |  |  |  |
| 5.8 x 10–3 1.2 x 10–2 | H2O film H2O droplets | 273-293 | Scheer et al, 1997 | WWFT/DT-FTIR/IC (a) |
| 1.2 x 10–2 | 1M NaOH(aq) |  |  |  |

# Comments

- The uptake kinetics has been measured using the two complementary techniques of the wetted-wall flow-tube at atmospheric and reduced (89-90 mbar) pressure and the droplet train technique, with combined FTIR and HPLC detection. A slight negative temperature dependence of  in the range indicated was observed.  The rate of uptake of ClNO on aqueous NaCl (up to 1M) and HCl (up to 1 M) was the same as on pure water.  The hydrolysis products were HONO and HCl, detected as NO2- and Cl- in solution.

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
|  | 0.01 | 273-293 |

Reliability

|  log (α) | ± 0.5 | 298 |
| --- | --- | --- |

Comments on Preferred Values

The recommendation accepts the value of Scheer et al.(1997). The results show that ClNO is reactive towards liquid water surfaces. The products are HCl and HONO; HONO was released to the gas phase, but the efficiency depended on the droplet acidity.

# References

Scheer, V., Frenzel, A., Behnke, W., Zetzsch, C., Magi, L., George, Ch. and Mirabel, Ph.: J. Phys. Chem. A, 101, 9359 (1997).