IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet VI.A1.15 HET_H2OL_15

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

This data sheet evaluated: 15th January 2009; last change in preferred values: 15th January 2009.

ClNO2 + H2O(l)  products

# Experimental data

| Parameter | [X]/ M | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- | --- |
| Uptake coefficients: ,ss,0 |  |  |  |  |
|  < 10–5 | H2O droplets | 280 | George et al, 1995 | DT-FTIR/IC (a) |
| ss = 4.8 x 10–6 | H2O film | 291 | Behnke et al., 1997 | WWFT-FTIR (b) |
| 0 = 3.4 x 10–6 | H2O film | 278 | Frenzel et al., 1997 | WWFT-FTIR (c) |
| 0 = 9.0 x 10–6 |  | 282 |  |  |
| 0 = 4.5 x 10–6 |  | 287 |  |  |
| 0 = (4.8±0.1) x 10–6 |  | 291 |  |  |
| ss = (2.6±1.8) x 10–6 a = (9±4) x 10–3 | H2O film | 274 | Fickert et al., 1998 | WWFT-MS (d) |

# Comments

- Uptake study using the droplet train technique at typically 13 to 40 mbar total pressure.  The trace gas density is monitored at the entry of the flow tube by FTIR.  The amounts of Cl- and NO3- in the droplets measured by ion chromatography was below the detection limit, therefore only an upper limit of  is given. The continuous flow of ClNO2 diluted in synthetic air at concentrations of up to 2500 ppm was generated by passing N2O5 through a 30 cm long wetted wall flow tube interacting with a 3M NaCl aqueous solution.

- Variable length (10-80 cm) wetted-wall flow tube at 1 bar of synthetic air.  The liquid film thickness was between 0.8 and 1.2 mm at a surface speed of 2-10 cm s-1. The gas flow rate was in the range 200-400 mL min-1 at 291K resulting in an average linear flow velocity of 15-30 cm s-1. The initial [ClNO2] was measured upstream, the unreacted ClNO2 was measured downstream of the WWFT using FTIR.  Between pure H2O and 1M NaCl  decreases by more than a factor of ten.

- Experimental details as (b). The uptake coefficients were obtained by fitting the initial measured time/position-dependent concentration profiles using a complex reaction mechanism including gas and liquid phase diffusion. The formation of ClNO2 was also observed when Cl2 interacted with the H2O film.

- Uptake study in a wetted-wall tubular flow reactor on a falling film of pure water and aqueous alkali halide salt solutions. The ClNO2 reactant and products was monitored using a differentially-pumped MS with electron impact ionization The value of ss remains unchanged upon addition of 1M NaCl whereas it increased upon addition of 0.1M OH-. Analysis of uptake rates measured under gas –phase diffusion controlled conditions (0.5 M KOH film) gave the cited value for the accommodation coefficient on aqueous surfaces, a = (9 ± 4) x 10-3.

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| ab | 9 x 10–3 | 273-298 |
| gss | 3 x 10–6 | 273-298 |

Reliability

|  log (α) | ± 0.5 | 298 |
| --- | --- | --- |

Comments on Preferred Values

The results show consistently that ClNO2 is non reactive towards liquid water surfaces. The recommended accommodation coefficient is based on the measurement of Fickert et.al,(1998).  The reactive uptake is controlled by hydrolysis which is very slow in pure water. The products have not been definitely identified.

# References

Behnke, W., George, Ch., Scheer, V. and Zetzsch, C.: J. Geophys. Res. 102, 3795 (1997).

Fickert, S., Helleis, F., Adams, J., Moortgat, G.K. and Crowley, J.N.: J. Phys. Chem. 102A, 10689 (1998).

Frenzel, A., Scheer, V., Sikorski, R., George, Ch., Behnke, W., and Zetzsch, C.: J. Phys. Chem. (1997).

George, Ch., Behnke, W., Scheer, V., Zetzsch, C., Magi, L., Ponche, J.L. and Mirabel, Ph.: Geophys. Res. Lett. 22, 1505 (1995).