IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet VI.A4.25 HET_SL_25

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet evaluated: June 2010; last change in preferred values: June 2010.

ClONO2 + H2O (aqueous sulphuric acid aerosol)  HONO2 + HOCl

# Experimental data

| Parameter | [H2SO4] wt% | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- | --- |
| ,ss,0 (ClONO2) |  |  |  |  |
| (3.2±0.8) x 10-3 | 95.6% H2SO4 |  | Rossi et al, 1987 | Knud-MS (a) |
| 2.6 x 10-3 3 x 10-4 | 65% H2SO4 75% H2SO4 | 210 230 | Tolbert, et al,, 1988 | Knud-MS (b) |
| 0.064±0.010 (3.1±0.5) x 10-3 (1.2±0.2) x 10-3 (3.9±0.7) x 10-4 (1.9±0.3) x 10-4 | 40% H2SO4. 60% H2SO4 65% H2SO4 70% H2SO4 75% H2SO4 | 218 215 215 220 230 | Hanson and Ravishankara, 1991a | WWFT-CIMS (c) |
| (8.1±1.3) x 10-2 (4.1±0.7) x 10-3 (2.1±0.35) x 10-4 | 40% H2SO4 57.5% H2SO4 75% H2SO4 | 220±5 | Golden et al., 1992; Williams et al., 1994; Manion et al., 1994 | Knud-MS (d) |
| (3.8±1.2) x 10-2 (6.1±2.0) x 10-3 (9.3±3.0) x 10-4 | 46.6% H2SO4 57.5% H2SO4 65% H2SO4 | 202 | Hanson and Ravishankara, 1994 | WWFT-CIMS (e) |
| (2.0±0.6) x 10-2 (2.5±0.7) x 10-3 (7.5±2.5) x 10-4 (3.0±1.0) x 10-4 | 50% H2SO4 60% H2SO4 65% H2SO4 70% H2SO4 | 197.5 205 211 218 | Zhang, Leu and Keyser, 1994 | WWFT-CIMS (f) |
| 2 x 10-3 | 65% H2SO4 | 250 | Hanson and Lovejoy, 1995 | AFT-CIMS (g) |
| 0.11 0.034 0.021 0.045 0.10 | 53% H2SO4 29% H2SO4,16.4%HNO3 5% H2SO4,41% HNO3 40% H2SO4,10% HNO3 5% H2SO4,41% HNO3 | 200 195 200 200 220 | Zhang, Leu and Keyser, 1995 | WWFT-CIMS (h) |
| (3.7±0.6) x 10-3 (5.60±0.84) x 10-2 (2.62±0.39) x 10-2 | 59% H2SO4 39% H2SO4 39% H2SO4 | 241 229 259 | Robinson et al., 1997 | DT-TDLAS (i) |
| 0.071±0.025 0.038±0.009 0.0094±0.003 | 36% H2SO4 43% H2SO4 54% H2SO4 | 245 248 253 | Ball et al., 1998 | AFT-CL (j) |
| 0.113±0.023 0.086±0.017 0.053±0.011 0.038±0.008 0.011±0.002 (1.6±0.3) x 10-4 (1.4±0.3) x 10-4 (1.1±0.2) x 10-4 (6.4±1.3) x 10-5 (2.5±1.0) x 10-5 0.019±0.004 0.042±0.016 | 36.5% H2SO4 36.5% H2SO4 45% H2SO4 45% H2SO4 55% H2SO4 75% H2SO4 75% H2SO4 75% H2SO4 75% H2SO4 75% H2SO4 44% H2SO4,4.6% HNO3 20% H2SO4,26% HNO3 | 203 230 203 230 203 270 250 230 217 200 203 205 | Hanson, 1998 | WWFT CIMS (k) |

# Comments

- Simultaneous flows of H2O (1.5x1013 molecule cm-3) and ClONO2 (9.4x1011 - 4.5x1013 molecule cm-3) were exposed to bulk 95.6% H2SO4 at ambient temperature;  is first order in [ClONO2] and declines with exposure time.

- The H2O vapor pressure in the flow reactor was 5.3x10-4 mbar (±30%). Uptake of ClONO2 at typical pressures of 6.4x10-3 mbar on 65% H2SO4/H2O.

(c)	Flowing aqueous H2SO4 film residence time of 20-30s. p(H2O) was ~ 1.3 x 10 -3 mbar and [ClONO2] was approx.1010 - 1011 molecule cm-3.  The temperature dependence of  was measured for the 60% and 70% H2SO4 solution:  none was found within the reported error limits.

(d) [ClONO2] was approx.1012 - 1013 molecule cm-3. The following analytical expression was obtained for the uptake/reaction probability () of ClONO2:  log  =1.87-0.074x[H2SO4] (wt%) (±15%) valid for the range 40 to 80% H2SO4 /H2O mixtures at 220K.

(e)	Quiescent liquid H2SO4 surface with CIMS detection. H2SO4 (46.6% to 65%) was applied as a cold liquid to the inner wall of the flow tube.

(f)	Walls coated with a 70% H2SO4 solution of approximately 0.1 mm thickness.  The partial pressure of H2O was held constant (5 ppm at 100 mbar pressure) throughout the temperature range 195 - 220K in order to control the acid concentration with temperature leading to [H2SO4] in the range 45 to 70% by weight.

(g)	High pressure (0.3 to 0.8 bar) flow tube using slow flow conditions and sub micron H2SO4 aerosol generated by homogeneous nucleation from the reaction of SO3 + H2O.  Particle size 60 - 250 nm diam. The uptake coefficient for the reaction of ClONO2 with 60 wt% sulfuric acid aerosol increases monotonically with particle size at 250 K.  The reactive-diffusive length (l, the effective liq. depth over which reaction occurs) derived from these experiments is 0.037 ± 0.007 m.

(h) Two methods of film preparation of defined ternary composition H2SO4/H2O/HNO3 at low temperatures resulted in identical values of  which does not change in the presence of HNO3, even at a limiting composition of 15% HNO3/30% H2SO4 at 195K.

(i)	Fast train of 200m H2SO4/H2O droplets traversing a flow tube with TDLAS detection.  Pressures = 13.3 mbar and droplet-gas interaction times of 2 to 20 ms.  The temperature of the droplets was inferred from the water partial pressure measured by TDL absorption.  A negative temperature dependence of ss was observed for T≥230K and ss slightly increased with increasing concentration of H2SO4 measured at 39, 54 and 69%.  A model involving neutral and acid catalysed mechanism for ClONO2 hydrolysis was used to extract valies of as and liquid phase rate constants by fitting data from several laboratories over a range of temperature and composition. The temperature dependence of as was given in the form as /(1- as) = exp(-17.89 + 4515/T).

(j)	High pressure (0.3 to 0.8 atm) flow tube using slow flow conditions and sub micron H2SO4 aerosol generated by homogeneous nucleation from the reaction of SO3 + H2O.  Particles of a narrow size range were selected with a DMA for each H2SO4 concentration used: mean size 95 nm, 104 nm and 63 nm radius  for 36, 43 and 54 wt% respectively. ClONO2 (30 to 200 ppb) detected by titrating with NO in a heated quartz tube, using TDLAS to monitor NO and also H2O vapor.  The average value of  was used to derive a value of l = 26 nm for the reacto-diffusive length at ~43% H2SO4

(k)	Uptake of ClONO2 measured in two flow reactors: a: Rotating wetted wall flow tube with sulfuric acid wall film (0.2 mm thickness). The pressure was 0.5 mbar He in the wall coated tube and 240 mbar of N2 in the aerosol flow tube.  The range of  [H2SO4] investigated was 36.5 to 55% H2SO4/H2O at 203K, 36.5 to 45.0% at 230K and 75% in the temperature range 200 to 270K. b: sub-micron aerosol (particle size 0.1m) 49±1% H2SO4/H2O . CIMS detection for ClONO2, HOCl and water vapor. Initial concentration was 5 x 1011 molecule cm-3 in both studies. The results for small sulfuric acid particles resulted in a lower limit of s>0.5. ClONO2 reaction probabilities were also measured on H2SO4 solutions containing significant amounts of HNO3. In contrast to previous reports, HNO3 was found to have a significant reducing effect on γ for ClONO2.

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| αs | 1 | 298 |
| kH2O /s-1 | 1.95 x 1010 exp(2800/T) | 190 - 280 |
| kH+ /M-1s-1 | 1.22 x 1012 exp(6200/T) | 190 - 280 |
| HClONO2/M.bar-1 | 1.6 x 10-6 exp(4710/T).exp[(-0.306 + 24.0/T).MH2SO4] | 200 - 280 |
| Dl /cm2s-1 | 5 x 10-8T/ | 180 - 240 |

MH2SO4= molarity H2SO4(Mol dm-3); wt = weight% H2SO4 ; X= mole fraction H2SO4

Reliability

|  log (α) | ± 0.1 | 298 |
| --- | --- | --- |
| log () | ±0.2 | 200 -280 |

Comments on Preferred Values

There is a large body of experimental data on the uptake of ClONO2 on H2SO4/H2O surfaces covering a relevant temperatures, humidity and sulphuric acid aerosol composition for the atmosphere between the surface and the lower stratosphere.  The results are generally consistent between the different studies which used both bulk and dispersed (aerosol) surfaces. The uptake leads to hydrolysis of ClONO2 and formation of HOCl and HNO3 which both transfer to the gas phase. The presence of HNO3 in the H2SO4/H2O solutions leads to a reduction in the uptake rate (Hanson, 1998; Zhang et.al, 1995). Based on uptake measurements of Hanson (1998) on HNO3/H2SO4/H2O solutions corresponding to conditions in the polar lower stratosphere (~5 ppb HNO3 in the gas phase), the g values would be approximately a factor of 2 lower than for H2SO4/H2O solutions.

Uptake rates show strong dependence on H2O content of the sulphuric acid solution/aerosol, ClONO2 decreasing in the range 20 - 70 wt% H2SO4. H2O content depends on both temperature and relative humidity and consequently there is a complex variation of  for atmospheric conditions: generally low temperature and high RH favour rapid reactive uptake with  values ~ 0.1 in 40% H2SO4 falling off to ~10-4 in 75% H2SO4. At low temperature the effects of composition dominates leading to weak negative T dependence of  .

These characteristics indicate that uptake is determined by chemical reaction in the liquid droplet and can be interpreted in terms of the resistance model.  Thus the overall uptake coefficient is given by eq.(2)

(1)

(2)

where H is the Henry’s solubility constant of ClONO2, Dl is the diffusion coefficient of ClONO2, and kI the first order rate constant for hydrolysis of ClONO2 in H2SO4/H2O solutions.

Robinson et al.(1977) presented a phenomenological model addressing solubility, diffusion and chemical reactivity of ClONO2,which accounts for the observed dependence of the uptake coefficients on concentration and temperature.  Two hydrolysis pathways are proposed, a direct reaction with H2O and an acid-catalysed reaction involving H+ ions to promote the dissociation: ClONO2 + H+HOCl + NO2+. The hydrolysis rate coefficient representing the two pathways was given in the form: kI = kH2O aw + kH+ aH+; here aw and aH+ are the activities of H2O and H+ in solution respectively. They extracted temperature and composition dependencies for the individual parameters, s and kI from a fit of their experimental  values using this model, together with a parameterisation of H based on solubility data given by Huthwelker et al (1995) for HOCl as a proxy for ClONO2. Dl was parameterized using the expression: Dl = CT/, with C evaluated from viscosity data for H2SO4/H2O solutions obtained by Williams and Long(1995).

Hanson (1998) has used a similar model, which gives  values as a function of mole fraction of H2SO4, X, which is defined for a given temperature and water activity (RH). Only a single direct hydrolysis reaction was used for kI. Composition dependent values of b were obtained from a fit of eq(1) to experimental X-dependent  values for 200-205K, assuming s =1.0: b = exp(-0.392-13.13X-50.914X2) (3). This simple expression can be used to calculate  from eq.1 with reasonable acuracy for specified values of H2SO4 wt% in the range 40 - 65% in and for temperatures near 200 K; at ≥70 wt% the observed  values are seriously underpredicted. Thus this formula only applies for only for a limited range of lower stratospheric conditions. Hanson also derived individual parameterisations for variation of H, Dl, H2SO4  acidity (aH+, aH2O) as a function of mole fraction of H2SO4, X, at temperatures near 200 K.

Shi et al (2001) have reported further analysis using these models for representation of uptake coefficients for ClONO2 hydrolysis and reaction with HCl in H2SO4 solutions.  They adopt a general mechanism involving both a direct and an acid-catalyzed channel for ClONO2 reaction with H2O and HCl, with the reactive species controlled by following equilibrium:

ClONO2(liq) + H+  HClONO2+(liq)				Keq

The hydrolysis rate constant is given by:

kI = kH2O aw + kH+aH+aw , 						(3)

where the acid catalysed rate constant, kH+, includes the term Keq, arising from the assumption that protonated species are in equilibrium. The values of Dl, H, H2SO4 acidity and water activity(aH+, aw) were parameterized independently of the experimental uptake measurements.

The thermodynamic model of Carslaw et al. (1995) was used to derive a parameterization of aw in terms of the mole fraction (X) of H2SO4, (X = wt%/(wt% + (100 – wt%)98/18):

aw = exp[(-69.775X - 18253.7X2 + 31072.2X3 - 25668.8X4)(1/T - 26.9033/T2)].

Note however that for atmospheric modelling aw is usually calculated from the local H2O mixing ratio and temperature. For the acid activity the Carslaw model was extended to include the acidity of pure water, to provide values of aH+ as a function of acid wt% (wt) in units of M dm-3 extending to dilute solution (wt ~ 0%):

aH+ = exp[60.51 - 0.095wt% + 0.0077wt%2 - 1.61x10-5wt%3- (1.76 + 2.52 x 10-4wt%2)T0.5

+ (-805.89+253.05wt%0.076)/T0.5.

Diffusion coefficients, Dl were estimated using the expression: Dl = CT/, with C = 5 x 10-8 cm2cP K-1s-1 (taken from Klassen et al., 1998). Viscosity data for H2SO4/H2O obtained by Williams and Long (1995) was re-parameterized to give a more general formulation covering the temperature range 200 – 300 K and 0 – 80wt% H2SO4:

 = AT-1.43 exp(448/T – T0))

A = 169.5 + 5.18wt% - 0.0825wt%2 + 3.27 x 10-3wt%3

T0 = 144.11 - 0.166wt% + 0.015wt%2 - 2.18 x 10-4wt%3

The variations of H and k1 with acid strength are constrained by the experimental values of H(k1)1/2, which is determined from experimental uptake coefficients using eq (2) for defined Dl.  Following Robinson et al.,(1997), the solubility of HOCl was used as proxy for ClONO2, and is given in the functional form:

H = Ho exp(B/T).exp(-St MH2SO4)					(4)

St = c + d/T								(5)

H(HOCl) was re-parameterized taking into account the higher temperature and wt% H2SO4 data of Donaldson et al (1997) which extended and improved that of Huthwelker et al (1995). The Setchenow coefficient, St, was assumed to depend on the molarity (rather than molality) of the H2SO4  solution. H was derived from indirect analysis of aerosol kinetics measurements of Hanson and Lovejoy (1995), which provided uptake coefficient, , and reacto-diffusive length, l, for hydrolysis of ClONO2 on 60% H2SO4 at 250 K. This provides a value for HClONO2 at a single temperature and to obtain the temperature dependence of H (and also of kI), use was made of the kinetic data for the ClONO2 + HCl reaction, for which the temperature dependence includes that of HClONO2 and kIHCl. Assuming the latter is diffusion limited (following Hanson, 1998) its temperature dependence is fixed, allowing extraction of the following parameters for calculation of the solubility of ClONO2: H0 = 1.6 x 10-6 , B = 4710, 
c = 0.306, and d = 24.0 in equations (4) and (5).

The rate coefficients for the direct and acid catalysed hydrolysis were expressed in Arrhenius form:

kH2O =AH2O. exp(-EH2O/T)

kH+ =AH+. exp(-EH+/T)

The values of kI for experimental conditions were calculated from eq 3, using the parameterisations for aH+, aH2O given above. The A and E values for the temperature dependence of kH  and kH2O were determined from a global fit to experimental uptake coefficients for both the ClONO2 hydrolysis and HCl reaction data, assuming the reaction ClONO2 + HCl is diffusion limited, in the same procedure as the determination of HClONO2 over a range of temperature.  The values obtained from fitting of the data from [Hanson, 1998, Ball et al., 1998, Robinson et al. 1997, Hanson and Lovejoy, 1995, Zhang et al., 1994, Manion et al. 1994, Hanson and Ravishankara, 1991, 1994] were:

AH2O= 1.95 x 1010 s-1		EH2O = 2800 K

AH+ = 1.22 x 1012  M-1s-1	EH+ = 6200 K

All three models give a good description of the experimental  values for the range of conditions used to derive the parameters. However the parameterisations for H, Dl, k1 and the other data on which they are based, differ considerably. The simpler parameterisation for b (eq.3) obtained by Hanson gives a reasonable representation of observed   values as a function [H2SO4], but only up to 65 wt%, and at temperatures around 200 K. The more complex parameterisation of Shi et al (2001) gives an excellent description of the experimentally observed data over a range of temperature 190 - 260 K at [H2SO4] in the range 35 - 75 wt%, as can be seen in the figure. The standard deviation of this model with respect to all experimental data used in the global fit was 32%(1)  The parameters of Shi et al., given in the Table above, are recommended as the preferred values for hydrolysis of ClONO2 covering most atmospheric conditions.

# References

Ball, S.M., Fried, A., Henry, B.E. and Mozurkewich, M.: Geophys. Res. Lett. 25, 3339, 1998.

Carslaw, K. S., Clegg., S.L. and Brimblecombe, J.Phys. Chem., 99 11,557, 1995.

Donaldson , D.J., Ravishankara, A.R., and Hanson, D.R.: J. Phys. Chem. A, 101, 4717, 1997

Golden, D.M., Manion, J.A., Reihs, C.M. and Tolbert, M.A., in CHEMRAWN VII: Chemistry of the Atmosphere: The Impact of Global Change, J. G. Calvert, Oxford University Press 1992.

Hanson, D.R. and Ravishankara, A.R.: J. Geophys. Res. 96, 17307, 1991a.

Hanson, D.R. and Ravishankara, A.R.: J. Phys. Chem., 98, 5728, 1994.

Hanson, D.R. and Lovejoy, E. R., Science, 267, 1326, 1995

Hanson, D.R.: J. Phys. Chem. A102, 4794 1998.

Huthwelker, T., Peter, Th., Luo, B.P., Clegg, S.L., Carslaw, K., and Brimblecombe, J.Atm.Chem., 81, 21, 1995

Klassen, J.K., Hu, Z., Williams, L.R.: J. Geophys. Res. 103, 16197-16202, 1998.

Manion, J.A., Fittschen, C.M., Golden, D.M., Williams, L.R. and Tolbert, M.A.: Isr. J. Chem. 1994.

Robinson, G.N., Worsnop, D.R., Kolb, C.E. and Davidovits, P.: J. Geophys. Res. J. Geophys. Res. 102, 3583-3601, 1997.

Rossi, M.J., Malhotra, R. and Golden, D.M.: Geophys. Res. Lett. 14, 127, 1987.

Shi, Q., Jayne, J.T., Kolb, C.E. Worsnop, D.R., and Davidovits, P.: 106, 24259-24274, 2001

Tolbert, M.A., Rossi, M.J., Malhotra, R. and Golden, D.M.: Science 238, 1258, 1987.

Williams, L.R., Manion, J.A., Golden, D.M. and Tolbert, M.A.: J. Appl. Meteorol. 33, 785, 1994.

Williams, L. R. and Long, F. S., J. Phys. Chem. 99, 3748-3751, 1995.

Zhang, R., Leu, M.-T. and Keyser, L.F.: Geophys. Res. Lett. 22, 1493, 1995.

Zhang, R., Leu, M.-T. and Keyser, L.F.: J. Phys. Chem. 98, 13563, 1994.

Figure 1: Temperature dependence of uptake coefficients for uptake of ClONO2 \by H2SO4/H2O surfaces plotted as a function of acid wt% in H2SO4/H2O solutions Lines show values calculated using parameters recommended in this evaluation, based on Shi et al.(2001). Points show selected experimental data taken from the table given in this datasheet, grouped in approximate acid wt% bands.