### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – 
Data Sheet HET_O_11

Datasheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission. 
The citation for this datasheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This datasheet last evaluated: June 2017; last change in preferred values: June 2017

HO2 + NH4NO3 (aq)  products

Experimental data

|  | RH / % | Temp./K | [Cu(II)] \ M | p(HO2) / mbar | Reference | Technique/ Comments |
| --- | --- | --- | --- | --- | --- | --- |
| Uptake coefficients: γ |  |  |  |  |  |  |
| 0.005± 0.002 | 29-70 | 292 | <10-4 | (0.6-6)×10-8 | George et al., 2013 | AFT-LIF (a) |

Comments

(c)	Uptake of HO2 (6×108 – 2×109 molecule cm-3) to NH4NO3 particles (mean surface area weighted diameter of 100-200 nm, aerosol surface area varied between 0 and 10-3 cm2 cm-3) at RH between 29 and 70 %. HO2 was generated by the photolysis of H2O in N2 or air and detected as OH (by LIF) following conversion in reaction with NO. Aerosol precursor solutions contained Fe and Cu at less than 1.8 μM. Separate experiments (not reported in the table) indicate a ( 70% higher uptake coefficient at short reaction times (< 10 s, in the mixing region) in comparison to the standard experiments (10 – 20 s). The uptake coefficient decreased by about a factor of 2 with the HO2 concentration increasing from 1.1×109 – 2.7×109 molecule cm-3; average values are given in the table.

Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| αb | > 0.2 | 290 - 300 |
| γ | 0.005 | 290 – 300 |
| kTMI (M-1 s-1) | 5 × 105 | 290 – 300 |
| k2 (M-1 s-1) | 2.4×109 exp(-2360/T) | 290 – 300 |
| k3 (M-1 s-1) | 1.6×1010 exp(-1510/T) | 290 – 300 |
| uncertainty |  |  |
| Δlog (γ) | 0.3 | 290 – 300 |
| Δlog (kTMI) | 1 | 290 – 300 |
| Δlog (k2,3) | 0.3 | 290 – 300 |

Comments on Preferred Values

While no study is available, in which bulk mass accommodation was rate limiting, we still prefer a value of b of > 0.2 in order to have an internally consistent recommendation among all aqueous substrates.

Our preferred value for γ is based on the uptake coefficient reported in the single study by George et al. (2013), which is in line with measurements on other aqueous substrates from the same group (George et al., 2013; Lakey et al., 2015, 2016), but in contrast with much higher values found by Taketani et al. (2008, 2009), as discussed on the datasheets for ammonium sulfate, ammonium bisulfate and halide solutions. Possible reasons include different flow tube residence times and surface to volume ratios, and possible contamination by transition metals.

Gershenzon et al. (1995) reported a value of 1.4×10-2 for the uptake coefficient on dry NH4NO3.

The uptake of HO2 in aqueous solution with pH > 5 is presently believed to be driven by self-reaction and acid-base dissociation of HO2 (pKa ~ 4.7) with formation of H2O2 (R2, R3). In the presence of transition metal ions (TMI) the reaction of HO2 and especially O2- (R4) can be important:

HO2 (g)					 O2- (aq) + H+ (aq)				R1

HO2 (aq) + HO2 (aq)			 H2O2 (aq) + O2 (aq) 			R2

O2- (aq) + HO2 (aq)  (+H2O(l))		 H2O2 (aq) + O2 (aq) + OH- (aq)		R3

O2- (aq) + TMI (aq)			 products					R4

If a first-order loss process for HO2 or O2- in the aqueous phase dominates (e.g. reaction with TMI such as Cu(II)), the uptake coefficient can be calculated from the expression below:

(1)

Heff = HHO2 (1+Keq/[H+]

Keq = 2.1  10-5 M at 298 K (Jacob, 2000)

HHO2 = 9.5  10-6 exp(5910/T) M atm-1 (Hanson et al., 1992)

kTMI is the second order rate coefficient for the reaction of HO2 and O2- with transition metal ions; the preferred value is justified in the datasheet VI.A3.10. For low viscosity aqueous solutions, the diffusivity of HO2 can be approximated by that in pure water (Schwartz, 1984; Thornton et al., 2008):

Dl = {110-5(T/298)}/(1.09108 exp(-0.068T) + 0.873)  cm2 s-1

where the denominator was derived from a fit to the water viscosity data of Hallett (1963). Dl needs to be assessed individually in presence of organic solutes that lead to strong changes to viscosity. The size dependent correction factor, with rp denoting the particle radius and lrd the reacto-diffusive length, assures proper representation when the kinetic regime changes from reaction-diffusion towards volume limited kinetics at low TMI concentrations.

In the absence of TMI, the rates of loss of aqueous-phase HO2 are quadratically dependent on [HO2]aq and [O2-]aq . The uptake coefficient is thus strongly dependent on the gas-phase concentration of HO2 and becomes small at low, relevant HO2 concentrations. Thornton and Abbatt (2005) suggest that the rate of loss of HO2 from the gas-phase (in molecule cm-3 s-1) is best described by a system in thermodynamic (Henry’s law) equilibrium so that (Thornton et al., 2008):

(2)

kaq can be calculated from the rate coefficients for R2 (k2) and R3 (k3) (Bielski et al., 1985) and the pH:

(3)

We suggest using equations (1) and (2) to consistently describe uptake of HO2 in presence and absence of transmission metal ions. As Figure 1 shows, equation (2) is consistent with the data point reported by George et al. (2013). The absence of dependence on relative humidity may result from a slightly decreasing pH with increasing humidity and at the same time an increasing radius due to the hygroscopic growth, with both effects possibly nullifying each other.

As discussed by Hanson et al. (1992) and Thornton and Abbatt (2005), the parameterization suggested here is very sensitive to the solubility of HO2 (HHO2), its temperature dependence and on the aerosol pH. Further experiments with systematic variation of different transition metals, aerosol pH and HO2 concentration would help to better assess the uncertainty of the parameterization.

We refer to recent publications for a more detailed description of the effect of different parameterisation schemes (Thornton et al., 2008; Macintyre and Evans, 2011).

# References

Bielski, B. H. J., Cabelli, D. E., Arudi, R. L., and Ross, A. B., J. Phys. Chem. Ref. Data, 14, 1041-1100, 1985.

George, I. J., Matthews, P. S. J., Whalley, L. K., Brooks, B., Goddard, A., Baeza-Romero, M. T., and Heard, D. E.: Phys. Chem. Chem. Phys., 15, 12829-12845, 2013.

Gershenzon, Y. M., Grigorieva, V. M., Ivanov, A. V., and Remorov, R. G., Faraday Discussions, 100, 83-100, 1995.

Hanson, D. R., Burkholder, J. B., Howard, C. J. and Ravishankara, A. R.: J. Phys. Chem. 96, 4979-4985, 1992.

Jacob, D. J., Atmos. Env., 34, 2131-2159, 2000.

Lakey, P. S. J., George, I. J., Baeza-Romero, M. T., Whalley, L. K., and Heard, D. E.: The J. Phys. Chem. A, 120, 1421-1430, 2016.

Lakey, P. S. J., Berkemeier, T., Krapf, M., Dommen, J., Steimer, S. S., Whalley, L. K., Ingham, T., Baeza-Romero, M. T., Pöschl, U., Shiraiwa, M., Ammann, M., and Heard, D. E.: Atmos. Chem. Phys., 16, 13035-13047, 2016.

Macintyre, H. L., and Evans, M. J., Atmos. Chem. Phys., 10, 7409-7414, 2010.

Morita, A., Kanaya, Y., and Francisco, J. S., J. Geophys. Res.-Atmos. 109, 2004.

Mozurkewich, M., McMurry, P. H., Gupta, A., and Calvert, J. G., J. Geophys. Res.-Atmos., 92, 4163-4170, 1987.

Schwartz, S. E., J. Geophys. Res.-Atmos., 89, 1589-1598, 1984.

Taketani, F., Kanaya, Y., and Akimoto, H., J. Phys. Chem. A, 112, 2370-2377, 2008.

Thornton, J., and Abbatt, J. P. D., J. Geophys. Res.-Atmos., 110, D08309, doi:10.1029/2004JD005402, 2005.

Thornton, J. A., Jaegle, L., and McNeill, V. F.: J. Geophys. Res. 113, doi:D05303

10.1029/2007jd009236, 2008.

Figure 1: Uptake coefficient of HO2 on NH4NO3 aerosol in absence of Cu(II). Symbols: data; solid line: calculated based on parameterization given by equation (2) for self-reaction only, for pH = 5.2, 100nm particle radius, and αb =0.3.