IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet V.A5.5 HNDT5

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

Data sheet last evaluated: March 2008; last change in preferred values: March 2008.

HNO3 + NAT

Experimental data

| Parameter | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Experimental uptake coefficients: , 0 |  |  |  |
| 0 > 0.3 0 > 0.2 | 191.5 200 | Hanson, 1992 | CWFT-CIMS a) |  |
| 0 >0.4 | 197 | Middlebrook et al., 1992 | Knud (b) |  |
|  = 0.165 HNO3•3H2O (NAT) 0.145 HNO3•2H2O (NAD) 0.13 HNO3•H2O (NAM) | 160-170 | Reinhardt, Fida and Zellner, 2003 | (c) |  |
| Partition coefficients: K(cm) |  |  |  |  |
| No reversible adsorption |  |  |  |  |

Comments

(a)	HNO3 deposited on ice condensed from the vapor phase onto the cold flow tube.  corrected for gas diffusion using estimated diffusion coefficients. Pressure = 0.6 mbar He.  Rapid uptake observed, but with increasing surface coverage of HNO3 the rate of uptake decreased.  The steady-state partial pressure of HNO3 over an ice surface with a coverage of approximately 1 monolayer of HNO3 was about a factor of five higher than the vapor pressure over NAT, showing that new hydrate was not formed.

(b)	Static chamber with time-dependent FTIR monitoring of depositing NAT film.  The thickness of the deposited NAT film was measured by optical interference in the range 4000 cm-1 to 7000 cm-1 assuming a refractive index of 1.45 for NAT.  pH2O = 2 x 10-4 mbar and pHNO3 = (5.3-13.3) x 10-7 mbar.  A doubling of the H2O left the uptake coefficient unchanged.

(c)	Slow flow reaction cell with DRIFTS for detection of adsorbed species and downstream FTIR for gas phase HNO3. Total pressure 10-30 mbar. At 170K and  [HNO3]= (2-5) x 1014 molecule cm-2 continuous uptake was observed with formation of crystalline HNO3•3H2O (NAT).  Monohydrates and dihydrates formed at higher pHNO3. Uptake coefficient independent of pHNO3.

Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| as | >0.2 | 190 - 240 |

Reliability

|  log (as) | ± 0.3 | 190 - 200 |
| --- | --- | --- |

Comments on Preferred Values

There have been few experimental studies of nitric acid interaction with specifically prepared HNO3-hydrate surfaces at temperatures and concentrations corresponding to hydrate thermodynamically stability regions. Under these conditions at T< 210 K uptake is continuous and irreversible.

References

Hanson, D. R.: J. Geophys. Res. Lett. 19, 2063 1992.

Middlebrook, A.M., Koehler, B.G., McNeill, L.S. and Tolbert, M.A.: Geophys. Res. Lett. 19, 2417 (1992).

Reinhardt, H.; Fida, M. and Zellner, R.: J. Mol. Struct. 661-662, 567-577 (2003).