# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet V.A1.28 HI28

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: September 2007; last change in preferred values: September 2007.

HOCl + ice

Experimental data

| Parameter | Temp./K | Reference | Technique/Comment |
| --- | --- | --- | --- |
| Experimental uptake coefficients: , 0 |  |  |  |
| 0 = 8.5 x10-2 | 180 200 | Oppliger, Allanic and Rossi, 1997 | Knud(a) |
| Partition coefficients KlinC (cm-1) |  |  |  |
| 79 | 191 | Hanson and Ravishankara, 1992 | CWFT-CIMS(b) |
| 3270 513 215 161 | 189 198 208 221 | Chu and Chu, 1999 | CWFT(c) |

Comments

(a)	Knudsen cell reactor using pulsed admission of HOCl and MS detection. The ice samples were generated from vapour phase deposition and resulted typically in a 20 µm thick film. A balancing H2O flow was set in order to keep the composition of the interface constant. Uptake rate constants for HOCl have been measured for doses <2.5 x 1014 molecule corresponding to <2.5% of a monolayer. At higher doses and in steady-state uptake experiments, strong saturation effects were found

(b)	HOCl was generated from the reaction HCl + Ca(ClO)2 and in-situ by the reaction of ClONO2 with ice surface; Uptake of gaseous HOCl (concentration ~ 2 x 109 molecule  cm-3) on pure ice was reversible at 191 K, the surface saturating within a few seconds, followed by rapid desorption when exposure ceased.  The fractional surface coverage in all the reported experiments did not exceed 0.01. A value of ~107 atm-1 was estimated for the Langmuir constant at 191K from the in-situ experiments; values of DHads and DSads of -58 ± 8 kJ mol-1 and -167 ± 41.8 J mol-1 K-1 respectively were estimated from data in the in the range 191 – 211K. HOCl did not adsorb on HNO3 doped ice.

(c)	Uptake of [HOCl] ~ 3 x 1010 molecule cm-3 on vapour deposited ice was reversible at 189 K, the surface saturating with a coverage of ~ 1 x 1014 molecule  cm-2 within a few seconds.  The uptake was followed by complete desorption when exposure ceased. Cited data for temperature dependence of partition coefficient at constant PHOCl = 8 x 10-7 mbar are taken from fig 4 of Chu and Chu (1999). A value of DHads of -34 ± 8 kJ mol-1 was estimated from the data.

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| 0 | 0.085 | 180 – 200 |
| Nmax / molecule cm-2 | 3 x 1014 |  |
| KLinC / cm | 3.06 x 10-6 exp(3840/T) | 190 -220 |

Reliability

|  log (0) | ± 0.3 | 180 – 200 |
| --- | --- | --- |
|  (KLinC) / cm | ± 0.5 | 205 |
|  (E/R) /K | ± 1200 |  |

Comments on preferred values

The available data show that the uptake rate of HOCl on ice is time dependent and absorption is  reversible and rather weak. Under these conditions uptake coefficients are difficult to measure and only one study, that of Oppliger et al (1997) using a Knudsen cell at very low doses, reports a value for g.

The only study reporting surface coverages measured from loss of HOCl from the gas phase is that of Chu and Chu (1999) and these are used here to derive partition coefficients, assuming Nmax = 3 x 1014 molecule cm-3.  Hanson and Ravishankara derive Langmuir constants indirectly from release of HOCl following its production in the ClONO2 + H2O reaction, but the values expressed as partition coefficients are considerably lower, probably due to the presence of the co-product HNO3 which is likely to compete strongly with HOCl for adsorption sites.  The temperature dependence observed by Chu and Chu (1999) gives a curved Van’t Hoff plot (see Fig 1) and the derived adsorption enthalpy cannot be considered reliable.  Nevertheless the values of K from a fit to a log K vs I/T plot of their data is recommended for use to estimate HOCl coverage for UTLS conditions.

References

Chu L. and Chu, L.T.: J. Chem. Phys.A., 103 691-699,(1999).

Hanson, D.R. and Ravishankara, A.R.: J. Phys. Chem. 96, 2682 (1992).

Oppliger, R., Allanic, A. and Rossi, M.J.: J. Phys. Chem. A 101, 1903 (1997).

Figure 1. Van’t Hoff plot of  adsorption equilibrium constants for uptake of HOCl on ice