IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation
Data Sheet HI40; V.A1.40

Datasheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission. 
The citation for this datasheet is: Crowley, J. N., Ammann, M., Cox, R. A., Hynes, R. G., Jenkin, M. E., Mellouki, A., Rossi, M. J., Troe, J., and Wallington, T. J., Atmos. Chem. Phys., 10, 9059-9223, 2010; IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This datasheet last evaluated: June 2014; last change in preferred values: April 2010

HONO + HI (Ice) → INO + H2O

Experimental Data

| Parameter | pHI /mbar | Temp./K | Reference | Technique/Comments |
| --- | --- | --- | --- | --- |
| Uptake coefficients: (ss |  |  |  |  |
| (2.9±0.9)×10-4 | 1.1×10-7 | 191 | Diao and Chu, 2005 | CWFT-MS (a) |
| (3.0±0.8)×10-2 | 8.9×10-5 | 191 |  |  |

Comments

(a)	30 m thick vapor-condensed H2O ice film doped with HI in the range 10-7 mbar to 10-5 mbar prior to exposure to HONO. The tabulated ( values are based on the geometric surface area of the film. Correction for pore diffusion into the ice substrate decreased the ( value by a factor of 6 to 50. INO could not be directly observed. It was suspected that INO formed on the ice film would react with I(ad) on the stainless steel surfaces between the ice film and the MS to form I2 that was detected. I(ad) would form from dissociative adsorption of HI. Correlation of relative rates with the reactions of HONO with HBr and HCl indicate the nucleophilic character of the reaction.

Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| αs | 0.02 | 180 - 220 |
| ks / cm2molecule-1s-1 | 8.0×10-19 | 180 – 220 |
| Reliability |  |  |
| ( log αs | ± 0.3 | 180 - 220 |
| ( log ks / cm2molecule-1s-1 | ± 0.3 | 180 - 220 |

Comments on preferred values

The single study by Diao and Chu (2005) reports rapid uptake of HONO to ice doped with HI. The conditions of these experiments were such that the HI-ice phase was not well defined above HI pressures above 10-6 mbar. The Eley Rideal type mechanism suggested by Diao and Chu (2000) is not supported as no HONO pressure dependence was reported. We therefore rather suggest the following expression for the uptake coefficient, describing a Langmuir-Hinshelwood type mechanism:

The surface coverage of HI should be taken as [HI]S = 3.0×1014 cm-2 at HI pressures between 10-8 and 10-7 mbar and as [HI]S = 8.0×1020 [HI] cm-2 at HI pressures above 10-7 mbar (see datasheet V.A1.32)

With ks and αS as recommended above, and KLangC(HONO) = 5.0×10-23 exp(5200/T) cm3 molecule-1 based on the value for KlinC and Nmax(HONO) = 3.0×1014 molecule cm-2 reported in the datasheet V.A1.11, good agreement with the data at pressures above 10-6 mbar is obtained. As is evident, at atmospherically relevant low pressures, where the conditions presumably fall into the ice stability regime, only the saturating surface coverage of 3 x 1014 cm-2 leads to agreement with experimental data, similar to the HCl case. This indicates that the interfacial concentration accessible to HONO is similar to the case of HCl and HBr at similar pressures. Given that the surface area may not be well characterized in the experiments, we recommend a large uncertainty associated with the surface reaction rate constant.

References

Diao, G. and Chu, L.T.: J. Phys. Chem. A 109, 1364-1373, 2005.

Figure 1: The recommended parameterization for p(HI) dependence of the uptake coefficient of HONO on ice in the presence of HI.