IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation
Data Sheet MD14

Datasheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission. 
The citation for this datasheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This datasheet last evaluated: June 2017; last change in preferred values: June 2017

OH  + mineral oxide (dust) surfaces  →  products

Experimental data

| Parameter | Substrate | pOH /mbar | Temp. /K | RH | H2O2 yield | H2O yield | Reference | Technique/ Comments |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Uptake coefficients: (, (0 |  |  |  |  |  |  |  |  |
| (6.3±2)×10-3 0.12±0.08 0.04±0.02 | SiO2 FeOx AlOx | 10-7 | 253-348 |  |  |  | Gershenzon et al., 1986 | FT-EPR(a) |
| (2±1)×10-3 (5±2)×10-3 (2±1)×10-4 | SiO2 Al2O3 TiO2 | 10-4 | 308 |  |  |  | Suh et al., 2000 | PBFT-LIF (b) |
| 0.11-0.44 | Al2O3 | 10-7 | 298 |  |  |  | Bertram et al., 2001 | CWFT-CIMS (c) |
| (3.2±0.7)×10-2 (8.4±1.7)×10-2 (9.8±2.2)×10-2 (4.5±0.5)×10-2 (7.2±0.8)×10-2 (8.4±1.2)×10-2 | SiO2 Al2O3 | 10-7 | 298 | 0 20 33 0 20 38 |  |  | Park et al., 2008 | PBFT-CIMS (d) |
| 0.19 0.074 γ0= 0.2±0.02 (0.18±0.5)/(1 + RH0.36 ) | ATD | 1.7×10-5 2.2×10-4 4.1×10-5 | 300 275-320 | <26 | 10 10 | 98 98 | Bedjanian et al., 2012 | CWFT-MS (e) |

Comments

(a)	Substrate material coated onto movable rod. Iron and aluminium were used with their native oxide layers. SiO2 was pre-treated with either chromic acid or hydrochloric acid. The uptake coefficients do not show a significant temperature dependence and average values are listed in the table.

(b)	Small pieces of SiO2 or α-Al2O3 and powders of anatase and rutile TiO2 (8.7 and 4.8 m2 g-1, respectively) were deposited on a frit and exposed to OH at a total pressure of a few mbar

(c)	Coated wall flow tube operated at 1 mbar and CIMS using SF6- for detection of OH which was produced by microwave discharge of H2 followed by reaction of H with O2 or NO2. The diffusion coefficient derived from pressure dependent loss rate measurements was 665±35 Torr cm2 s-1.

(d)	Al2O3 and SiO2 powder mixed with halocarbon wax and coated onto glass beads. Total pressure 133 mbar. OH loss rates derived from measured OH loss and comparison to a reference with halocarbon wax only. Uptake coefficients derived using the virtual cylindrical flow tube approximation (tube with equal surface area to gas volume ratio) and assuming that the fraction of reactive surface area corresponds to the volume fraction of the component in the coating mixture. OH produced by microwave discharge of H2 and reaction of H with O2, leading to OH via H + HO2. OH detection with SF6- as reagent ion.

(e)	ATD films (85 ± 10 m2 g−1 surface area) formed from a suspension in ethanol, followed by drying and baking at 100-150°C in vacuo. UV irradiation (315-400 nm, JNO2 = 0.002-0.012 s-1). OH ((0.4 – 5.2) × 1012 molecule cm-3) was produced via reaction of H atoms with NO2 or of F atoms with H2O and was detected as HOBr following reaction with Br2. Observed first order loss rates were corrected for diffusion with D0 = 640×(T/298)1.85 Torr cm2 s-1 to obtain the geometric uptake coefficient, which did not depend on coating mass, and thus the true surface explored is not exactly known. First-order loss rates exhibited significant deactivation with integration over long times resulting in more loss than a monolayer equivalent, indicating catalytic loss. Due to the uncertainties related to the surface area and to the extent products diffusing into the interior of the films, only initial uptake coefficients were reported. UV radiation had no effect on the uptake kinetics.

Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| ( | 0.2 | 280-320 |
| Reliability |  |  |
| log (() | ±0.7 | 280-320 |

Comments on Preferred Values

The recommendation is based on the initial uptake coefficient obtained for ATD (though this is not an authentic airborne dust) and for experiments at the lowest partial pressures of OH and the lowest total pressure in the flow tube (data by Bedjanian et al. (2012) and Bertram et al. (2001)). Experiments at higher partial pressures of OH indicate saturation or deactivation above 10-5 mbar. Experiments at higher total pressures in the reactor are likely affected by diffusion that is in addition difficult to be taken into account for the configurations of experiments by Park et al. (2008) and Suh et al. (2000). No temperature dependence of the uptake coefficient was observed.

In view of the inconsistent relative dependence of the uptake coefficient on relative humidity for the Bedjanian et al. and Park et al. data sets, we prefer a humidity independent uptake coefficient with large error bounds.

Various mechanisms have been suggested by which OH is transformed into H2O and H2O2 (Suh et al., 2000; Bogart et al., 1997; Fisher et al., 1993; Gershenzon et al., 1986). In view of secondary chemistry involving both secondary sources (including gas phase) and sinks (on mineral oxides) for H2O2 it is difficult to determine the H2O2 yield unambiguously.

References

Bedjanian, Y., Romanias, M. N., and El Zein, A., J. Phys. Chem. A, 117, 393-400, 2013.

Bertram, A. K., Ivanov, A. V., Hunter, M., Molina, L. T., and Molina, M. J., J. Phys. Chem. A, 105, 9415-9421, 2001.

Bogart, K. H. A., Cushing, J. P., and Fisher, E. R., J. Phys. Chem. B, 101, 10016-10023, 1997.

Fisher, E. R., Ho, P., Breiland, W. G., and Buss, R. J., J. Phys. Chem., 97, 10287-10294, 1993.

Gershenzon, Y. M., Ivanov, A. V., Kucheryavyi, S. I., and Rozenshtein, V. B., Kin. Catal., 27, 923-927, 1986.

Park, J. H., Ivanov, A. V., and Molina, M. J., J. Phys. Chem. A, 112, 6968-6977, 2008.

Suh, M., Bagus, P. S., Pak, S., Rosynek, M. P., and Lunsford, J. H., J. Phys. Chem. B, 104, 2736-2742, 2000.

Figure 1: Dependence of uptake coefficient of OH on mineral dust on OH partial pressure.

Figure 2: Dependence of uptake coefficient of OH on mineral dust on relative humidity