IUPAC Task Group on Atmospheric Chemical Kinetic  data Evaluation – Data Sheet VI.A4.11 HET_SL_11

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task group on Atmospheric chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet evaluated: May 2009; last change in preferred values: May 2009.

N2O5 + H2O (aqueous sulphuric acid aerosol)

# Experimental data

| Parameter | RH/ % | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- | --- |
| Uptake coefficients: ,ss,0 |  |  |  |  |
| 0.10  0.01 0.139  0.009 | 1-10 RH 1-10 | 293 274 | Mozurkewitch and Calvert, 1988 | AFT-CL (a) |
| 0.12±0.03 0.14±0.03 0.10±0.02 0.10±0.02 | 40% H2SO4 60% H2SO4 70% H2SO4 75% H2SO4 | 226 | Hanson and Ravishankara, 1991a | WWFT-CIMS (b) |
| 0.058±0.006 | 73% H2SO4 | 283 | Van Doren et al., 1991 | DT-TDLAS (c) |
| 0.055±0.010 | 74%-96% H2SO4 | 220±5 | Golden et al., 1992; Williams et al., 1994; Manion et al., 1994 | Knud-MS (d) |
| 0.06±0.04 0.103±0.006 0.12±0.016 0.148±0.011 0.086±0.009 0.146±0.036 0.102±0.011 0.077±0.019 | 79-84% H2SO4 64-81% 57-76% 63-76% 61-63% 69-71% 65-69% 54-64% | 293 273 260 247 247 230-234 231-234 225-231 | Fried et al., 1994 | AFT-CL(e) |
| 0.076±0.018 0.081±0.032 0.061±0.013 0.109±0.024 0.077±0.016 0.090±0.020 | 60% H2SO4 60% H2SO4 70% H2SO4 70% H2SO4 80% H2SO4 80% H2SO4 | 270 230 296 230 270 230 | Hanson and Lovejoy, 1994 | AFT-CIMS(f) |
| 0.11 0.034 0.021 0.045 0.10 | 53% H2SO4 29% H2SO4,16.4%HNO3 5% H2SO4,41% HNO3 40% H2SO4,10% HNO3 5% H2SO4,41% HNO3 | 200 195 200 200 220 | Zhang, Leu and Keyser, 1995 | WWFT-CIMS (g) |
| 0.075±0.047 | 65% H2SO4 | 210-230 | Beichert and Finlayson-Pitts, 1996 | Knud-MS (h) |
| 0.023  0.004 0.038  0.012 0.060  0.020 0.050  0.008 | 90 % RH, 17% H2SO4 58.5% RH, 40% H2SO4 19.5% RH, 59% H2SO4 8.5% RH, 66% H2SO4 | 297 | Hu and Abbatt, 1997 | AFT-CIMS/OPC (i) |
| 0.187  0.028 0.154  0.023 0.159  0.024 0.086  0.0129 | 69% H2SO4 69% H2SO4 39% H2SO4 39% H2SO4 | 240 260 231 255 | Robinson et al., 1997 | DT-TDLAS (j) |
| 0.11 0.02 0.092 0.021 0.045 0.10 | 60% H2SO4 55% H2SO4,5%HNO3 45% H2SO4,15%HNO3 59%H2SO4,0.08%HNO3 58% H2SO4,1-2% HNO3 | 210-230 202 230 | Hanson, 1997 | WWFT and AFT-CIMS(k) |
| 0.033  0.004 0.028  0.008 0.036  0.004 0.049  0.009 0.091  0.019 0.092  0.013 | 8-80% RH, 26.3-55% H2SO4 40% RH, 49% H2SO4 40% RH, 48%H2SO4 40% RH, 44% H2SO4 40% RH, 42% H2SO4 40% RH, 42% H2SO4 | 298 298 288 278 268 263 | Hallquist et al., 2000 | AFT-CL/SMPS (l) |
| 0.045 0.045  0.013 0.030 0.075 0.061 | 0.7 % RH, 81% H2SO4 2.9 % RH, 76% H2SO4 7.7 % RH, 70% H2SO4 16 % RH, 63% H2SO4 28.4 % RH, 55% H2SO4 | 295±1 | Kane et al., 2001 | AFT-CIMS/SMPS (m) |
| 0.050 0.044 0.033 0.016 | 38 2% H2SO4 32% H2SO4,10%HNO3 17% H2SO4,34%HNO3 9% H2SO4,48% HNO3 58% H2SO4,1-2% HNO3 | 193.6 | Wagner et al., 2005 | Static Reactor-FTIR (o) |

# Comments

- Atmospheric pressure aerosol flow tube with N2O5 ( 1013 molecule cm-3)measured by a modified chemiluminescence method, via thermal dissociation to NO3 and titration with NO, which was detected. Aerosols generated in a constant output atomiser, dried, and size selected with a differential mobility analyser (DMA) coupled to a condensation particle counter (CPC). The monodisperse aerosol was then equilibrated at controlled humidity before entry into the flow tube. The typical diameter, dmean was 0.08-0.2 m, with surface area density of 1 – 5 x 10-5 cm2/cm3. Uptake coefficients were determined from the first order rate constants for N2O5 decay, corrected for wall loss, which were linearly dependent on surface area. Diffusion limitation was negligible for the size range used. The uptake of N2O5 on H2SO4/H2O was independent of RH in the range 1-10%.

(b)	Wetted wall flow tube coupled to CIMS detection.  Aqueous H2SO4 film residence time of 20-30s.  P(H2O) was ~ 1.3 x 10 -3 mbar.  The temperature dependence of  was measured for the 60% and 70% H2SO4 solution:  none was found within the reported error limits.

(c)	Fast train of 200m 73% H2SO4/H2O droplets traversing a flow tube with TDLAS detection.  Pressures = 13.3 mbar and droplet-gas interaction times of 1-2 ms.

(d)	Knudsen cell technique using MS detection. P(N2O5) was 0.4 to 10 x 1011 molecule cm-3.   value of 0.02-0.03 -independent of temperature, concentration (74 to 96% H2SO4/H2O).   value corrected for saturation effects.

(e)	High pressure (0.3 to 0.8 atm) flow tube using slow flow conditions and sub micron H2SO4 aerosol generated by homogeneous nucleation from the reaction of SO3 + H2O.  Particle size 60 - 250 nm diameter at 225 to 293K, with H2SO4 54 to 82wt%. N2O5 (30 to 200 ppb) detected by titrating with NO in a heated quartz tube, using TDLAS to monitor NO and also H2O vapor.

(f)	Kinetics of N2O5 hydrolysis on sulfuric acid aerosol measured in laminar flow reactor at 825 mbar of N2, using CIMS detection.  The aerosol surface area was determined by UV extinction using Mie theory.  The H2SO4 particle concentration were in the range 5 - 100  x 104 particles cm-3 with diameters between 0.2 to 0.4 m.  Initial N2O5 concentration was of the order of 1 to 5 x 1013 molecule cm-3.  The uptake measurements on 60% H2SO4 at 230 K may have been influenced to some extent by HNO3 uptake and hence partial saturation.

(g)	Wetted wall flow reactor - CIMS.  Liquid sulfuric acid films were applied to the cooled wall of a horizontally mounted tube . Total pressure = 0.53 mbar of He with partial pressure of N2O5 of 6.7 x 10-7 mbar.  The  values decrease with increasing HNO3 content hence decreasing temperature at constant H2O and HNO3 partial pressure.  On the binary H2SO4/H2O surface =0.1 independent of temperature.  In the temperature range 195 to 220 K  may be expressed as  = -0.379+0.00213T at PH2O=5 x10-7 mbar and PHNO3=6.7 x 10-7 mbar.

(h)	Knudsen flow reactor using MS detection. N2O5 concentration was in the range 3 to 90 x 1011 molecule cm-3.

(i)	Atmospheric pressure aerosol flow tube with detection of N2O5 (7 x 1012 molecule cm-3) by CIMS using I- reagent ion.  The aerosols were generated in an ultrasonic nebuliser and were equilibrated with the ambient humidity before entry into the flow tube.  The size distribution, measured with an optical particle counter (OPC), was used to calculate the surface area of the aerosol in the flow tube. The peak in the surface area distribution, dmax was between 2 and 4 m. The counter was calibrated by collection of aerosol of known composition in a aqueous trap (assumed 100% efficient) and measurement of the electrical conductivity of the trapped electrolyte. Uptake coefficients were determined from the first order rate constants for N2O5 decay, corrected for wall loss (Brown correction), and for diffusion limitation to the particle surface assuming an average diameter,dmax, of the non-monodisperse aerosol. The first order rate constant for the title reaction scaled linearly with the aerosol surface area. Cited  errors on  is ±1 precision; the estimated potential systematic error arising mainly from measurement of the SA was ±25%. HNO3 accumulation in the aerosol was insignificant.

(j)	Fast train of 200m H2SO4/H2O droplets traversing a flow tube with TDLAS detection.  Pressures = 13.3 mbar and droplet-gas interaction times of 2 to 20 ms.  The temperature of the droplets was inferred from the water partial pressure measured by TDL absorption.  A negative temperature dependence of ss was observed for T≥230K and ss slightly increased with increasing concentration of H2SO4 measured at 39, 54 and 69%.  Model involving neutral and acid catalysed mechanism for N2O5 hydrolysis fitted data from several laboratories.

(k)	Flow reactors with sulfuric acid wall film (0.2 mm thickness) and sub-micron aerosol (particle size 0.1m) - CIMS detection. The pressure was 0.5 mbar He in the wall coated tube and 240 mbar of N2 in the aerosol flow tube.  Initial [N2O5] was 5 x 1011 molecule cm-3 for the aerosol and 5 x 1011 molecule cm-3 for the bulk liquid experiment.

(l)	Uptake study using a sulfuric acid aerosol of typically 1.5 to 4x105 particles cm-3 of 240 to 400 nm peak diameter flowing down a laminar flow tube and interacting with N2O5 whose concentration was in the range 2.5-12.5 x 1012 cm-3.  The  value is independent of rh at 298 K and has a strong negative temperature dependence at approximately 45%wt in the stated range.  The reaction mechanism is complex and is controlled by competing reactions of direct and acid-catalyzed hydrolysis whereas ionic dissociation of N2O5 into NO3- and NO2+ does not seem to play a role at low temperatures.

(m)	Atmospheric pressure flow tube with contact times between 1.5 and 7s once the 100nm diameter aerosol was well mixed with N2O5 that was detected using CIMS.  The  value increased monotonously to  = 0.05±0.025 at 100%rh for both ammonium salts which was identical to the average value for the uptake of N2O5 on H2O at 300K.

(n)	N2O5 uptake experiment in an aerosol flow tube at characteristic N2O5 concentrations of 500ppb coupled to NO2 detection using a chemiluminescence detector after thermal decomposition of N2O5 and following NO3 titration with NO.  Typical aerosol number densities were (6-10)x105 particles cm-3.  The  values were independent of RH in the range 8 - 80%, and hence on aerosol H2O content in the range 24.3 - 64.5wt% H2SO4 . showed a negative temperature dependence at RH = 40%.

(o)	Uptake of N2O5 prepared in situ in a large aerosol cold chamber (AIDA) equipped with aerosol metrology instrumentation, gas-and particular phase H2O detection using hygrometers and FTIR extinction measurement capabilities.  Saturated ternary solutions (STS) consisting of H2SO4/HNO3/H2O were formed by the interaction of N2O5 between the initial 38 wt% H2SO4/H2O background aerosol with H2O vapour from ice-coated chamber walls.  The decrease of  with increasing mixing ratio of HNO3 is attributed to the nitrate effect at low temperatures.

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| α | 0.042 | 298 |
| α | 2.3 x 10-5.exp(2240/T) | 240 -300 |
| r | [(7353/T) - 24.83]-1 | 210 - 300 |

Reliability

|  log (α) | ± 0.1 | 298 |
| --- | --- | --- |
| log () | ±0.3 at 50% RH | 260 -305 |

Comments on Preferred Values

There is a large body of experimental data on the uptake of N2O5 on H2SO4/H2O surfaces covering the wide range of temperature and humidity relevant for the atmosphere between the surface and the lower stratosphere.  The results are generally consistent between the different studies which used both bulk and dispersed (aerosol) surfaces. At room temperature  shows little dependence on RH in the range 8 - 80%, and hence on aerosol H2O content in the corresponding range 20 - 70 wt% H2SO4. However at low temperatures there is a fall off in with decreasing water content. shows a distinct negative temperature dependence at T> 230 K, but at lower temperature the temperature dependence becomes positive. The uptake leads to hydrolysis of N2O5 and formation of HNO3 which transfers to the gas phase.  However at low temperatures the increased solubilty of HNO3 in the H2SO4/H2O particles leads to a reduction in the uptake rate.

The lack of a dependence on the water content of H2SO4/H2O surfaces and the negative temperature dependence at T>230 K suggests that uptake is controlled by a surface process, either mass accommodation or surface reaction. It is suggested by Robinson et al (1997) that the change in behaviour at low temperature is due to uptake under these conditions becoming limited by the rate of hydrolysis of N2O5 in bulk liquid phase.  They presented a phenomenological model which accounts for the observed dependence of the uptake coefficients on concentration and temperature.  Two hydrolysis pathways are proposed, a direct reaction with H2O and an acid-catalysed reaction involving dissociation of N2O5 promoted by H+ ions.

The recommended expression for  uses a resistance-model formulation but with an empiracle representation of the temperature dependent liquid phase resistance due to chemical reaction, r:

 =

The recommended value of ab is based on a linear least squares fit to all data at T>240 K, plotted in the form ln[/(1-)] vs 1/T.  The temperature dependence of the r term was determined by plotting the difference term (1/obs-1/) against 1/T and using linear regression to evaluate the empiracle relationship between 1/r and temperature.  Fig1 shows calculated uptake coefficients as a function of temperature compared with the experimental data determined for a range of [H2SO4].

# References

Badger, C. L.; Griffiths, P.T.; George, I.; Abbatt, J.P.D. and Cox, R.A.: J. Phys. Chem. A 110, 6986 2006.

Beichert, P. and Finlayson-Pitts, B. J., J. Phys. Chem., 100, 15218, 1996

Griffiths, P.T. and Cox, R.A.: Atmos. Sci. Lett., 10, 159-163, (2009)

Hallquist, M., Stewart, D.J., Baker, J. and Cox, R.A.: J. Phys. Chem. 104A, 3984 2000.

Hallquist, M., Stewart, D.J., Stephenson, S.K. and Cox, R.A.: Phys. Chem. Chem. Phys. 5, 3453 2003.

Fried, A; Henry. B. E.; Calvert, J. G.; Mozurkewich, M. J. Geophys. Res., 99, 3517, 1994.

Folkers, M., Mentel, Th F.Mentel and Wahner, A.: Geophys.Res.Lett., 30, No12, 1644, doi:10.1029/2003GL017168, 2003.

Golden, D.M., Manion, J.A., Reihs, C.M. and Tolbert, M.A. in CHEMRAWN VII: Chemistry of the Atmosphere:  The Impact of Global Change, J. G. Calvert (ed.), Oxford University Press 1992.

Hanson, D. R., Geophys.Res.Lett., 24, 1087, 1997.

Hanson, D.R. and Ravishankara, A. R., J. Geophys. Res. 96, 17307 1991a.

Hu, J.H. and Abbatt, J.P.D.: J. Phys. Chem. A101, 871, 1997.

Kane, S.M., Caloz, F. and Leu, M.-T.: J. Phys. Chem. 105A, 6465, 2001.

Mentel, T.F, Sohn,M. and Wahner, A.: Phys. Chem. Chem. Phys. 1, 5451, 1999.

Mozurkewich, M. and Calvert, J.G.: J. Geophys. Res. 93, 15889, 1988.

Robinson, G.N., Worsnop, D.R., Kolb, C.E. and Davidovits, P.: J. Geophys. Res. J. Geophys. Res. 102, 3583, 1997.

Thornton, J.A., Braban, C.F. and Abbatt, J.P.D.: Phys. Chem. Chem. Phys 5, 4593-4603, 2003.

Van Doren, J.M., Watson, L.R., Davidovits, P., Worsnop, D.R., Zahniser, M.S. and Kolb, C.E.: J. Phys. Chem. 95, 1684, 1991.

Wagner, R., Naumann, K.-H., Mangold, A., Möhler, O., Saathoff, H. and Schurath, U.: J. Phys. Chem. A 109, 8140 (2005).

Williams, L.R., Manion, J.A., Golden, D.M. and Tolbert, M.A.: J. Appl. Meteorol. 33, 785, 1994.

Zhang, R., Leu, M.-T. and Keyser, L.F.: Geophys. Res. Lett. 22, 1493, 1995.

Zhang, R., Leu, M.-T. and Keyser, L.F.: J. Geophys. Res. 100, 18845, 1995a.

Figure 1: Uptake coefficients for uptake of N2O5 \by H2SO4/H2O aerosol plotted as a function of temperature. -X- recommended functional form; o = observations with error limits; filled circles: predicted accommodation coefficient from fit to data at T>260 K.

Figure 2: Uptake coefficients for uptake of N2O5 \by H2SO4/H2O aerosol plotted as a function of acid strength. Data selected in temperaure range ± 10 K around 295, 265, and 235 K.

Figure 3: Uptake coefficients for uptake of N2O5 \by H2SO4/H2O aerosol plotted as a function of temperature. Data selected in RH range ± 10% around 80, 60, 40% and <30% RH.

Figure 4: Uptake coefficients ( for uptake of N2O5 \by H2SO4/H2O aerosol plotted in functional form : ln(/(1-) vs 1/T. Data selected in temperature range 240 - 298 K.