### IUPAC Task Group on Atmospheric chemical Kinetic Data Evaluation – Data Sheet V.A1.14 HI14

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This Data sheet last evaluated: December 2007: ; last change in preferred values: December 2007.

N2O5 + ice

# Experimental data

| Parameter | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Experimental uptake coefficients: ,ss |  |  |  |
|  = 0.028  0.011 | 195 | Leu, 1988 | CWFT-MS (a) |  |
|  > 1 x 10-3 | 185 | Tolbert et al., 1988 | Knudsen-MS (b) |  |
|  = 0.034  0.008  = 0.023  0.008 | 188 | Quinlan et al., 1990 | Knudsen-MS (c) |  |
|  = 0.024  0.007 | 201 | Hanson and Ravishankara, 1991 | CWFT-CIMS (d) |  |
|  = 0.01 – 0.02 | 191 | Hanson and Ravishankara, 1992, 1993 | CWFT-CIMS (e) |  |
|  = 0.02  0.002 | 200 | Seisel et al., 1998 | Knudsen-MS (f) |  |
| ss = (7  3) x 10-4 | 185 | Zondlo et al., 1998 | Knudsen- MS/FTIR (g) |  |

# Comments

(a)	Flow reactor at 0.36 - 0.67 mbar. The ice film was made by vapour deposition. N2O5 (initial concentration  1x1013 molecule cm-3) detected as its NO2+ ion-fragment.  HNO3 found to build up on the surface.  calculated using geometric ice surface area.

(b)	N2O5 (initial concentration  1013 molecule cm-3) detected as its NO+ and NO2+ ion-fragments. Surface adsorbed HNO3 (reaction product) was detected by thermal desorption spectrometry. Coincidence of fragment ions from HNO3 (reaction product) and N2O5 enabled only an upper limit to the uptake coefficient (calculated using geometric ice surface area) to be determined.

- N2O5 (initial concentration  1013 molecule cm-3) detected as its NO+ and NO2+ ion-fragments. Gas-phase HNO3 reaction product was detected following thermal desorption, TD, as its HNO3+, NO+ and NO2+ ion-fragments.  (calculated using geometric ice surface area) showed a pronounced time dependence, maximising after several seconds of exposure, and then decreasing again. The value of  quoted in the Table is the maximum value observed. The two values quoted represent results obtained on ice made from freezing a bulk solution (0.034  0.008 ) or vapour deposited ice (0.023  0.008). The TD yield of HNO3 was found to match the amount of N2O5 lost to the surface (3-7 x 1016 cm-2), suggesting that the uptake is purely reactive.

- Low initial N2O5 concentration (109-1010 molecule cm-3) measured using I- chemi-ionisation. The 7-15 m thick ice film was made by vapour deposition. Deactivation of the surface was seen to take place during exposures of several minutes duration.  was calculated from first-order decay constants at low exposure times, using the geometric surface area of the ice.

- Same experimental procedure as (d), but with the ice film thickness varied between  1 and 40 m.  was found to vary between  0.01 and 0.02.

- The ice surface was formed by either vapour deposition or by freezing liquid water. The N2O5 concentration was  1.5 x 1011  molecule cm-3.

- The ice surface was formed by vapour deposition, [N2O5] was varied between  2 x 1010 and 3 x 1011 molecule cm-3. The uptake coefficient reported represents a steady-state value, presumably for an HNO3 contaminated ice surface. Surface analysis was performed using reflection-absorption infra-red spectroscopy and revealed the presence of H3O+ and NO3- ions in an H2O / HNO3 amorphous solution at 185 K and the loss of crystalline structure of the ice.

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
|  | 0.02 | 190 - 200 |

Reliability

|  log () | ± 0.15 | 190 - 200 |
| --- | --- | --- |

Comments on Preferred Values

The preferred value of  is taken from the works of Hanson and Ravishankara (1991, 1992, 1993) who used very low N2O5 concentrations, and applies to a pure (i.e. non passivated) ice surface. The less detailed study of Seisel et al. (1998) at 200 K is in accord with this recommendation. Hanson and Ravishankara (1991) observed deactivation of the surface after a few minutes of exposure to N2O5, whereas Quinlan et al  (1990) observed increasing reactivity with time. This is most likely due to the use by Quinlan et al. (1990) of high concentrations of N2O5 at the surface, causing surface melting by HNO3.

Evidence for an efficient hydrolysis of N2O5 to HNO3 (probably present mainly in ionised form at the surface) is provided by the observation of surface deactivation for N2O5 uptake (Hanson and Ravishankara, 1991), thermal desorption experiments Quinlan et al. (1990) and infrared surface analysis of ions such as NO3- and H3O+ (Zondlo et al, 1998; Horn et al., 1994; Koch et al., 1997). At appropriate combinations of N2O5 concentration and temperature, NAT is formed (Hanson and Ravishankara, 1991).

# References

Hanson, D. R., and Ravishankara, A. R.: J. Geophys. Res. 96, 5081-5090, 1991.

Hanson, D. R., and Ravishankara, A. R.: J. Phys. Chem. 96, 2682-2691, 1992.

Hanson, D. R., and Ravishankara, A. R.: J. Phys. Chem. 97, 2802-2803, 1993.

Horn, A. B., Koch, T., Chesters, M. A., McCoustra, M. R. S., and Sodeau, J. R. S.: J. Phys. Chem. 98, 946-951, 1994.

Koch, T. G., Banham, S. F., Sodeau, J. R., Horn, A. B., McCoustra, M. R. S., and Chesters, M. A.: J. Geophys. Res. 102, 1513-1522, 1997.

Leu, M. T.: Geophys. Res. Lett. 15, 851-854, 1988.

Seisel, S., Flückiger, B., and Rossi, M. J.: Ber. Bunsenges. Phys. Chem. 102, 811-820, 1998.

Tolbert, M. A., Rossi, M. J., and Golden, D. M.: Science, 240, 1018-1021, 1988.

Quinlan, M. A., Reihs, C. M., Golden, D. M., and Tolbert, M. A.: J. Phys. Chem. 94, 3255-3260, 1990.

Zondlo, M. A., Barone, S. B., and Tolbert, M. A.: J. Phys. Chem. A 102, 5735-5748, 1993.