IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet VI.A1.6 HET_H2OL_6

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

This data sheet first evaluated: May 2009.

NH3 + H2O (water droplets)

# Experimental data

| Parameter | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Uptake coefficients: ,ss,0 |  |  |  |  |
| 0.040+0.03-0.005 | 299 | Bongartz et al., 1995 | LJ-IC (a) |  |
| 0.097  0.009 | 290 | Ponche, George and Mirabel, 1993 | DT-FTIR/HPLC (b) |  |
| 0.1 (pH=0.5 - 3.0) 0.06 (pH=8) 0.006 (pH=10 - 13) 0.35 (pH=0.5 - 3.0) | 291 291 291 260 | Shi et al., 1999 | DT-FTIR/MS (a) |  |

# Comments

(a)	Uptake of NH3 in a liquid jet of dilute HCl solution with continuous measurement of NH4+ in the collected jet waters. Contact time of 0.1 ms to 0.8 ms virtually free of saturation effects in the liquid phase. The  values for air (+He) as carrier gas agreed very well with those measured in He ( = 3.5 x 10-2 in air vs. 4.0 x 10-2 in He).

(b)	Gas interaction with monodisperse (70 µm to 110 µm diameter) droplet train propagating axially in a low pressure (46 mbar to 93 mbar) flow tube. Uptake determined by ion chromatographic analysis of collected aqueous phase was independent of pH in the range 4.2 to 11.5 but dependent on the contact time and pressure. The value listed in the table has been corrected for gas phase diffusion.  The measured average uptake coefficient obs was (2.4 ± 1.0) x 10-2 at 93 mbar N2 and 290 K, obtained by extrapolation to zero interaction time.

(b)	Uptake experiment of gas phase NH3 on train of droplets whose size was in the range 150-300 m entrained in a flowing mixture of helium and water vapour (between 2.9 and 23.3 mbar). The reaction time was between 2 and 15 ms, the ammonia concentration was in the range 1013 to 2x1014 cm-3 and was monitored using a VUV lamp emitting at = 121.6 nm. The theoretical framework included gas phase diffusion of ammonia, mass accommodation, dissolution, bulk and surface reaction whose relative contributions changed with pH.  The effective Henry's law solubility was measured in the range 264 to 350 K: log(H) = -3.221 +1396/T. The uptake coefficient was dependent on pH, falling rapidly from ~ 0.08 at pH=7 to 0.006 at pH=10. At low pH there is a negative temperature dependence of , which is attributed to accommodation controlled uptake.  At high pH, NH3 is less soluble and uptake controlled by a surface complex is suggested. Co-deposition with SO2 enhanced the ammonia uptake to values corresponding to acidic solutions.

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| a | 0.1 | 290 |
| a | 0.1 | 260 -300 |

Reliability

|  log () | ± 0.3 | 290 |
| --- | --- | --- |

Comments on Preferred Values

The uptake coefficients on pure water, measured using the droplet train technique are somwhatt larger than onto dilute HCl in a liquid jet. Both methods require correction for gas phase diffusion and for saturation effects.  On balance the DT experiment gives more reliable data we base the recommendation of the results of Ponche et al.(1993) and Shi et al., 1999), who also determined the temperature dependence at pH = 1. The value is higher than usually observed for the mass accommodation coefficient, a, for uptake on pure water, and the strong dependence of g on pH (Shi et al., 1999), indicates a direct chemical interaction of NH3 at the surface, e.g. by protonation.

References

Bongartz, A., Schweighoefer, S., Roose, C. and Schurath, U.: J. Atmos. Chem. 20, 35 (1995).

Ponche, J.L., George, Ch. and Mirabel, Ph.: J. Atmos. Chem. 16, 1 (1993).

Shi, Q., Davidovits, P., Jayne, J.T., Worsnop, D.R. and Kolb, C.E.: J. Phys. Chem. A 103, 8812 (1999).