### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet V.A4.0 HET_SL_0

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: January 2009; last change in preferred values: January 2009

O3 + H2SO4  →  products

Experimental data

| Parameter | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Uptake coefficients:  |  |  |  |  |
| < 1  10-6 | 300 – 270 | Baldwin and Golden, 1979 | Knudsen-MS (a) |  |
| (4.79  1.38)  10-11 (75 wt.% H2SO4) | 223 | Olszyna et al., 1979 | (b) |  |
| < 1  10-6 | 195 | Dlugokencky and Ravishankara, 1992 | CWFT-CLD (c) |  |
| (1.2  0.08)  10-6 (98 wt.% H2SO4) | 239 | Il’in et al, 1992 | UV (d) |  |
| (1.6  0.08)  10-6 (98 wt.% H2SO4) | 258 |  |  |  |
| (1.75  0.07)  10-6 (98 wt.% H2SO4) | 273 |  |  |  |

Comments

(a)	No evidence for uptake of O3 to H2SO4 surface which contained less than 5 % water.

(b)	Static experiment with H2SO4 coated on glass beads in a round bottom flask. O3 analysed ex-situ. Slow loss of O3 was observed over several hours to derive the values of  listed.

(c)	 2 mm thick (frozen) H2SO4 films were prepared from a bulk solution of  50 or 97 wt%. [O3] was either 5  108 or 2  109 molecule cm-3. The geometric surface area was used to calculate .

(d)	Static reactor with O3 measured using optical absorption at 254 nm. Initial [O3] was 1-6  1015 molecule cm-3.

Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
|  | < 10-6 | 200 – 220 K |

Comments on Preferred Value

The studies of the uptake of O3 to various H2SO4 surfaces confirm that the interaction is very weak with uptake coefficients lower than 10-6. Olszyna et al. (1979) measured comparable uptake coefficients on pure H2SO4 and H2SO4 doped with various cations (Ni2+, Cu2+, Cr3+, Al3+, Fe3+ NH4+ and Mn2+. Doping with Fe2+ resulted in  values close to 10-9.  Uptake coefficients of the order of 10-8 to 10-9 were obtained on frozen H2SO4 surfaces at 217 – 263 (Harker and Ho, 1979).  The preferred value is based on the uptake coefficients obtained in the flow tube experiments of Dlugokencky and Ravishankara (1992) which were carried out at stratospheric temperatures and using low [O3].

References

Baldwin, A. C. and Golden, D. M.: Science 206, 562-563, 1979.

Dlugokencky, E. J. and Ravishankara, A. R.: Geophys. Res. Lett. 19, 41-44, 1992.

Harker, A. B. and Ho, W. W.: Atmos. Environ. 13, 1005-1010, 1979.

Il'in, S. D., Selikhanovich, V. V., Gershenzon, Y. M. and Rozenshtein, V. B.: Sov. J. Chem. Phys. 8, 1858-1880, 1991.

Olszyna, K., Cadle, R. D. and Depena, R. G.: J. Geophys. Res. 84, 1771-1775, 1979.