### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation
Data Sheet V.A2.1 MD1

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: January 2009; last change in preferred values: January 2009.

O3  + mineral oxide (dust) surfaces

Experimental data

| Parameter | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Uptake coefficients:  |  |  |  |  |
| ssBET = (1.40.35) x 10-6 (SiO2) | 295 | Il'in et al., 1992 | SR-UV (a) |  |
| 0BET = (85) x10-5 (α-Al2O3 powder) 0BET = (1.80.7)x10-4 (α- Fe2O3 powder) 0BET = (53)x10-5 (SiO2 powder) 0BET = (2.70.9)x10-5 (China loess) 0BET = (63)x10-5 (Saharan Dust, ground) 0BET = (42)x10-6 (Saharan Dust, sieved, <50µm) | 296 | Michel, Usher and Grassian, 2002 | Kn-MS (b) |  |
| 0BET = (1.40.3) x10-4 (α-Al2O3 powder, 25µm) ssBET = 7.6 x 10-6 (α-Al2O3 powder, 25µm) 0BET = (93)x10-5 (α-Al2O3 powder, 1µm) 0BET = (2.00.3)x10-4 (α- Fe2O3 powder) ssBET = 2.2 x 10-5 (α- Fe2O3 powder) 0BET = (6.30.9)x10-5 (SiO2 powder) 0BET = (31)x10-5 (kaolinite) 0BET = (2.70.8)x10-5 (China loess sand) 0BET = (62)x10-5 (Saharan Dust, ground) ssBET = 6 x 10-6 (Saharan Dust, ground) 0BET = (2.70.9)x10-6 (Saharan Dust, sieved, <50µm) | 295 | Michel, Usher and Grassian, 2003 | Kn-MS (c) |  |
| 0pd = (5.5 3.5)x10-6 (Saharan Dust, unheated, 8.4x1012 cm-3 O3) 0pd = (3.5 3.0)x10-4 (Saharan Dust, unheated, 5.4x1010 cm-3 O3) sspd = (2.2 1.3)x10-6 (Saharan Dust, unheated, 8.4x1012 cm-3 O3) sspd = (4.8 2.8)x10-5 (Saharan Dust, unheated, 5.4x1010 cm-3 O3) | 296 | Hanisch and Crowley, 2003 | Kn-MS (d) |  |
| 0BET = 1.0x10-5 (α-Al2O3, [O3]=1013 cm-3) 0BET = 1.0x10-6 (α-Al2O3, [O3]=1014 cm-3) | 298 | Sullivan et al., 2004 | SR-UV (e) |  |
| 0BET = 6x10-6 (Saharan dust, [O3]=2x1012 cm-3) 0BET = 2x10-7 (Saharan dust, [O3]= 1014 cm-3) | 298 | Chang et al., 2005 | SR-UV (e) |  |
| sspd = (2.70.3)x10-6 (Kaolinite powder) sspd = (7.80.7)x10-7 (CaCO3 powder) | 298 298 | Karagulian and Rossi, 2006 | Kn-MS (f) |  |
| ssBET = (3.50.9)x10-8 (α-Al2O3, dry, [O3]=9.8x1014 cm-3) ssBET = (4.50.9)x10-9 (α-Al2O3, 19 % RH, [O3]=1.1x1015 cm-3) ssBET = (1.00.3)x10-7 (α-Fe2O3, dry, [O3]=6.8x1014 cm-3, dry) ssBET = (5.01.2)x10-8 (α-Fe2O3, dry, [O3]=1.9x1014 cm-3, dry) ssBET = (4.41.1)x10-9 (α-Fe2O3, 41 % RH, [O3]=8.5x1014 cm-3, dry) ssBET = (9.02.3)x10-9 (α-Fe2O3, 43 % RH, [O3]=7.5x1013 cm-3, dry) | 298 | Mogili et al., 2006 | SR-UV/FTIR aerosol chamber (g) |  |
| Partitioning coefficients: KlinC |  |  |  |  |
| 1.6 x 103 cm (Saharan dust) | 296 | Hanisch and Crowley, 2003 | Kn-MS (h) |  |

Comments

(a)	Observation of O3 in reaction vessels using optical absorption at 254 nm in the presence of Ar. Typical ozone and Ar pressures were 1.3-13 and 2.6 mbar, respectively.  Mechanistic information and the temperature dependence of the decay rate constants were given for quartz, glass and water surfaces.

(b)	Bulk powder samples generated by gently heating an aqueous slurry of the powder on the sample support. The ozone concentration was 1.9x1011 cm-3.  The initial and steady state  values shown in the table have been calculated using the BET surface area in the linear mass dependent regime.

(c)	Bulk powder samples generated by gently heating an aqueous slurry of the powder on the heated sample support. The ozone concentration was varied from 1011 cm-3 to 1012 cm-3.  The initial and steady state  values shown in the table have been calculated using the BET surface area in the linear mass dependent regime.  The uptake coefficients were independent of the ozone concentration within the range given. A small temperature dependence of  was observed, leading to an activation energy of 74 kJmol-1.  The steady state uptake coefficients were reported for an interaction time of 4.5 h. Owing to the fact that the amount of consumed O3 is always on the order of 1 to 2 monolayers regardless of the duration of the interaction leads the authors to the conclusion that the O3/mineral dust interaction is catalytic in nature.

(d)	Powder samples were prepared by dispersing an aqueous or methanol based paste onto the sample holder and evacuating overnight. Some samples were heated to 450 K prior to use. Steady state uptake coefficients were calculated (extrapolated) based on a bi-exponential fit to the observed uptake curves. The tabulated initial and steady state  values were corrected using a pore diffusion model.  The relative O2 product yield varies from 1.0 to 1.3  0.05 for unheated and heated (450K, 5h under vacuum) samples, respectively. Release of water correlated with the ozone concentration. Passivated samples could be reactivated by evacuation overnight.

(e)	Static reaction cell (Pyrex) equipped with detection of O3 using UV absorption at 254 nm resulting in a typical signal-to-noise ratio of 1 at 2x1012 molecule cm-3 and 1s integration.  The dust powder was coated onto the surface by applying a methanol slurry and drying without heating. The BET surface area of separate coatings was measured using Kr adsorption at 77 K (2.2 m2/g for alumina and 14 m2/g for Saharan dust). The first-order decays of O3 have been measured over the first 10 s and have been converted to the listed considered as 0, as a slightly decreased slope can be recognised at times later than 10 s. 0 seemed to be constant for O3 concentrations between 1012 and 1013 cm-3 for alumina and was inversely proportional to the O3 concentration above 1013 cm-3 for both alumina and Saharan dust.  does not change with humidity in the range 0 to 75% rh.  A significant degree of reactivation of exposed samples was detected ranging from a few to over 50% of the initial value of  by storing the spent samples in a container purged with dry and CO2-free air for a few days.  No products were detected.

(f)	Steady state and pulsed uptake experiment on powder substrates using a Knudsen flow reactor equipped with molecular beam modulated MS detection.  The  values displayed were obtained using a pore diffusion model for the data on kaolinite and CaCO3. For CaCO3, also a sample of roughened marble was used to represent a flat CaCO3 surface and to avoid corrections to the uptake coefficient. The uptake coefficient obtained was 3.5 x 10-5, which is a factor 50 higher than the one obtained for the CaCO3 powder sample after pore diffusion correction. Further experiments were performed with Saharan dust and Arizona test dust, for which only uptake coefficients referred to the geometric sample surface area are reported. The reactivity of the ATD was slightly lower than that of CaCO3, while that of SD was slightly higher. The SD sample showed a factor of 2 decrease in reactivity with O3 concentration increasing from 3.5 x 1012 to 1.0 x 1013 cm-3. In general, initial uptake coefficients were a factor of 3 to 10 higher than steady state values. The only gas phase product detected was O2. The O2 yield per O3 consumed showed significant variation from 0.0 to 2.0.

(g)	Powder samples were evacuated prior to use and then injected into a 0.15 m-3 chamber. The aerosol was not further characterized. The surface to volume ratio of the aerosol used to calculate uptake coefficients was taken from the injected sample mass and the BET surface area of the sample measured separately. O3 was detected using FTIR in the range of up to 40 ppm and with UV absorption below 10 ppm. Under dry conditions, for α-Fe2O3, turnover numbers, defined as number of O3 molecules lost divided by the number of available surface sites, were 2 and above, indicating catalytic reactivity. For α-Al2O3, the turnover number remained smaller than 1, in spite of a large excess of O3. The uptake coefficient was decreasing with increasing O3 concentration and strongly decreasing by a factor of 50 with humidity increasing from dry to 58 % relative humidity.

(h)	Saharan dust samples were deposited on a sample holder in the form of an ethanol paste. The experiment was aimed at determining NO to NO2 oxidation rates as a function of O3 concentration. The rates were fitted assuming Langmuir adsorption of both NO and O3 prior to reaction. The value of KLinC given in the table has been derived from KLangC = 4 x 10-12 cm3 reported by the authors and an assumed Nmax  = 4 x 1014 cm-2.

Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
|  | 1500 [O3 (cm-3)]-0.7 | 298 |

Reliability

|  log () | ± 0.5 | 298 |
| --- | --- | --- |

Comments on Preferred Values

Given the different techniques used to obtain kinetic data, the data agree fairly well, when considering the strong dependence of the steady state uptake coefficients on ozone concentration, which has also been discussed in most of the studies cited. The initial uptake coefficients are more difficult to compare as they seem to depend more on the way the samples were exposed, and possibly also on the treatment of the samples prior to the experiment (heating, evacuation). Also the time resolution of the experiments is different, which makes the interpretation of initial uptake coefficients difficult without explicit kinetic modelling of especially the static and aerosol experiments. Probably because of the small steady state reactivities, interpretation of the kinetic data using the BET surface area of the powder samples in the linear mass dependent regime or using pore diffusion theory led to fairly consistent results. We therefore use only uptake coefficients derived from steady state uptake data that are referred to the BET surface area in our evaluation. The earlier study by Alebic-Juretic et al. (1992) is in qualitative agreement with the studies cited here, but does not directly provide quantitative kinetic data.

Considering the steady state values only, the Saharan dust, kaolinite, Al2O3, Fe2O3 and CaCO3 agree surprisingly well with each other. We used the available Saharan dust data to obtain a recommendation of the uptake coefficient as a function of ozone concentration in the range of 1010 to 1013 cm-3, for relative humidity below 5%.

All studies note the potential effects of humidity, which has a significant effect on spectroscopic signatures on alumina observed in DRIFTS experiments (Roscoe and Abbatt, 2005; see below). Sullivan et al. (2004), however, found no humidity dependence in their kinetic experiments using the same type of samples. On the other hand, Mogili et al. (2006) report a significant humidity dependence of the uptake coefficient, which was reduced by a factor of 50 from dry to 60% relative humidity for Fe2O3 and a factor of about 10 from dry to 20% relative humidity for Al2O3.

Given the consistent dependence of steady state uptake coefficients of the ozone concentration, the rate limiting step in the mechanism of the reaction of ozone with mineral dust seems to be common among the different materials investigated, even in the atmospherically relevant concentration range around 1012 cm-3. This mechanism may be represented by the following reactions, which have been consistently proposed in most studies:

O3  + SS  SS-O  + O2			(1)

SS-O + O3  SS-O2 + O2		(2)

Therein, SS denotes a reactive surface site, which are likely Lewis acid sites as present on alumina or Fe2O3 that are susceptible to dissociative adsorption of O3, a Lewis base. Whether this first dissociation reaction occurs as a Langmuir-Hinshelwood or Eley Rideal reaction is not clear. But since desorption of O3 from a dust surface has never been observed, Langmuir type adsorption is unlikely, even though Hanisch and Crowley (2003b) reported a Langmuir constant for O3 to explain the oxidation behaviour of NO on the dust surface. We therefore do not recommend a value for KLinC. It is more likely that complete oxidation of all available SS to SS-O, which is the reactive species towards NO and O3, explains the saturation behaviour. It is likely that in the experiment by Hanisch and Crowley (2003a), the O3 loss kinetics was driven by uptake due to reaction (1) at the lower O3 concentration. An oxidised surface species SS-O is consistent with IR spectroscopic features observed by Roscoe and Abbatt (2006). The formation of the second, peroxy species, by reaction (2) has been suggested based on a study of O3 decomposition on MnO (Li et al., 1998), but could not be observed by Roscoe and Abbatt (2006), because the IR signature was outside the wavelength region they probed.

Overall, reactions (1) and (2) can explain turnover rates of ozone of up to two, which have indeed been observed, along with the formation of O2 as a product (Mogili et al., 2006; Karagulian et al., 2006). Slow decomposition of SS-O2 and self reaction of SS-O have been suggested to release reactive SS again, which would establish a catalytic cycle for ozone destruction. The time scale of reactivation observed in the experiment was on the order of a day.

The role of humidity in the reaction mechanism is not clear. On one hand, hydroxylated surface sites seem to be involved in reaction (1) (Hanisch and Crowley, 2003a), while water can be involved in removing oxygen from SS-O as observed by Roscoe and Abbatt (2006), which would also explain the strong humidity dependence observed by Mogili et al. (2006), though at very high O3 concentrations. Therefore, humidity on one hand can competitively adsorb to reactive sites and therefore reduce the uptake coefficient, while on the other hand, it may lead to reactivation of oxidised surface sites.

In view of the significant uncertainties related to the mechanism (details of reactions (1) and (2), humidity dependence, reactivation processes), we have allowed for a relatively large uncertainty associated with the recommended steady uptake coefficients.

References

Alebic-Juretic, A., Cvitas, T., and Klasinc, L.: Ber. Bunsenges. Phys. Chem., 96, 493-495, 1992.

Chang, R. Y. W., Sullivan, R. C., and Abbatt, J. P. D.: 32, 2005.

Hanisch, F., and Crowley, J. N.: Phys. Chem. Chem. Phys., 5, 883-887, 2003b.

Hanisch, F., and Crowley, J. N.: Atmos. Chem. Phys., 3, 119-130, 2003a.

Ill'in, S. D., Selikhanovich, V. V., Gershenzon, Y. M., and Rozenshtein, V. B.: Sov. J. Chem. Phys., 8, 1858-1880, 1991.

Karagulian, F., and Rossi, M. J.: Int. J. Chem. Kin., 38, 407-419, 2006.

Li, W., Gibbs, G. V., and Oyama, S. T.:, J. Am. Chem. Soc., 120, 9041-9046, 1998.

Michel, A. E., Usher, C. R., and Grassian, V. H.: Geophys. Res. Lett., 29, 2002.

Michel, A. E., Usher, C. R., and Grassian, V. H.: Atmos. Environ., 37, 3201-3211, 2003.

Mogili, P. K., Kleiber, P. D., Young, M. A., and Grassian, V. H.: J. Phys. Chem. A, 110, 13799-13807, 2006.

Roscoe, J. M., and Abbatt, J. P. D.: J. Phys. Chem. A, 109, 9028-9034, 2005.

Sullivan, R. C., Thornberry, T., and Abbatt, J. P. D.: Atmos. Chem. Phys., 4, 1301-1310, 2004.

Usher, C. R., Michel, A. E., Stec, D., and Grassian, V. H.: Atmos. Environ., 37, 5337-5347, 2003.

Steady state uptake coefficients reported for mineral dust