IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet Ox_VOC21

Datasheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission. The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, (http://iupac.pole-ether.fr).

This datasheet last evaluated: August 2018; last change in preferred values: August 2018

O3 +               (camphene)  products

Rate coefficient data

| k/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| (9.0  1.7) × 10-19 | 296  2 | Atkinson et al., 1990 | S-CL/GC (a) |
| Relative Rate Coefficients |  |  |  |
| (4.3  0.5) × 10-19 | 298  2 | Johnson et al., 2000 | RR-GC (b) |
| (5.5 ( 1.2) × 10-19 | 298  2 | Gaona-Colmán et al., 2017 | RR-FTIR (c) |
| 9.8 × 10-18 exp[(-859 ± 53)/T] | 288-311 |  |  |

camphene is 2,2-dimethyl-3-methylene-bicyclo[2.2.1]heptane

Comments

- k determined from the observed first-order rate of ozone decay (measured with a chemiluminescence analyzer) in the presence of known excess concentrations of camphene (measured by GC-FID). Experiments were carried out at a total pressure of 980 mbar in a 160 L Teflon chamber. k was corrected to account for the presence of a 10 % monoterpene impurity of comparable ozone reactivity in the camphene sample, which was tentatively identified as the structurally-similar monoterpene, -fenchene.

- The concentrations of camphene and ethene (the reference compound), with cyclohexane to scavenge HO radicals, were monitored by GC-FID in a 50 L collapsible Teflon chamber at 760 Torr (1013 mbar) pressure of purified air in the presence of O3.  The measured rate coefficient ratio k(O3 + camphene)/k(O3 + ethene) is placed on an absolute basis using k(O3 + ethene) = 1.55 × 10-18 cm3 molecule-1 s-1 at 298 K (IUPAC, current recommendation).

- The concentrations of camphene and ethene or o-cresol (the reference compounds), with cyclohexane to scavenge HO radicals, were monitored by GC-FID in a 50 L collapsible Teflon chamber at 760 Torr (1013 mbar) pressure of purified air in the presence of O3. Experiments performed at 298 K carried out using both ethene and o-cresol as reference compounds; with only ethene used at other temperatures. The measured rate coefficient ratios k(O3 + camphene)/k(O3 + ethene) and k(O3 + camphene)/k(O3 + o-cresol) are placed on an absolute basis using k(O3 + ethene) = 6.82 × 10-15 exp(-2500/T) cm3 molecule-1 s-1 and k(O3 + o-cresol) = 2.6 × 10-19 cm3 molecule-1 s-1 at 298 K (IUPAC, current recommendations).

Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| k /cm3 molecule-1 s-1 | 5.0 × 10-19 | 298 |
| k /cm3 molecule-1 s-1 | 9.0 × 10-18 exp(-860/T) | 285-315 |

Reliability

|  log k | ± 0.30 | 298 |
| --- | --- | --- |
| (E/R | ± 500 | 285-315 |

Comments on Preferred Values

The preferred value of E/R is based on the sole temperature dependence study of Gaona-Colmán et al. (2017), which covered only a narrow temperature range. Confirmatory studies of the temperature dependence are required. The preferred 298 K rate coefficient is a rounded average of the relative rate determinations of Johnson et al. (2000) and Gaona-Colmán et al. (2017), which are in good agreement. The absolute determination of Atkinson et al. (1990) required correction for the presence of an impurity, but the reported value of k lies within the assigned uncertainty range in the preferred value.

The reaction proceeds by initial addition of O3 to the C=C bond to form a “primary ozonide (POZ)” which rapidly decomposes to form two sets of “primary” carbonyl product plus Criegee intermediate, as shown in the schematic below:

Camphenilone (3,3-dimethyl-bicyclo[2.2.1]heptan-2-one) is expected to be formed in conjunction with the Criegee intermediate CH2OO (channel (a)), and has been reported as a significant product, formed with a yield of (36 ± 6) % (Hakola et al., 1994). Channel (b) is expected to form HCHO and the Criegee intermediate C9H14OO, although there have been no reported measurements of the yield of HCHO.

The Criegee intermediate, CH2OO (formed from channel (a)), is expected to be almost fully stabilised at atmospheric pressure, by analogy with the -pinene system (Nguyen et al., 2009). Based on reported kinetic data (summarised and evaluated in datasheets CGI_1 to CGI_12), the major fate of CH2OO under tropospheric conditions is expected to be removal via bimolecular reactions, particularly with (H2O)2. Partial stabilisation of the C9 Criegee intermediate, C9H14OO (formed from channel (b)), has also been inferred by Hasson et al. (2001), based on scavenging with added H2O and observation of the corresponding products.

Atkinson et al. (1992) have reported an upper limit HO yield of ≤ 18 % for the reaction of O3 with camphene, indicating that HO formation from the decomposition of C9H14OO is also a minor route. The formation of HO via the accepted decomposition mechanism (involving abstraction of a -hydrogen via a vinyl hydroperoxide intermediate) may be inhibited owing to the only -hydrogen in C9H14OO being at the bridgehead of a constrained bicyclic structure, as discussed by Rickard et al. (1999) and Nguyen et al. (2009) for the structurally-similar isomeric Criegee intermediate formed from -pinene ozonolysis. The alternative well-documented decomposition route, via a dioxirane intermediate (e.g. Johnson and Marston, 2008), leads to the formation of a lactone (4,4-dimethyl-3-oxa-bicyclo[3.2.1]octan-2-one), which has been reported to be a significant product (yield  20 %) by Hakola et al. (1994). If stabilized, C9H14OO may also potentially react with H2O under atmospheric conditions. Based on the results of Hasson et al. (2001), this leads mainly to formation of the hydroxyalkyl hydroperoxide shown in the schematic, with minor formation of camphenilone and H2O2.

References

Atkinson, R., Aschmann, S. M. and Arey, J.: Atmos. Environ., 24A, 2647, 1990.

Atkinson, R., Aschmann, S. M., Arey, J. and Shorees, B.: J. Geophys. Res., 97, 6065, 1992.

Gaona-Colmán, E., Blanco, M. B., Barnes, I., Wiesen, P. and Teruel, M. A.: RSC Adv., 7, 2733, 2017.

Hakola, H., Arey, J., Aschmann, S. M. and Atkinson, R.: J. Atmos. Chem., 18, 75, 1994.

Hasson, A. A., Ho, A. W., Kuwata, K. T. and Paulson, S. E.: J. Geophys. Res., 106, 34143, 2001.

Johnson, D. and Marston, G.: Chem. Soc. Rev., 37, 699, 2008.

Johnson, D., Rickard, A. R., McGill, C. D. and Marston, G.: Phys. Chem. Chem. Phys., 2, 323, 2000.

Nguyen, T. L., Peeters, J. and Vereecken, L.: Phys. Chem. Chem. Phys., 11, 5643, 2009.

Rickard, A. R., Johnson, D., McGill, C. D. and Marston, G.: J. Phys. Chem. A, 103, 7656, 1999.