# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet P16

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

This data sheet updated: 16th May 2002.

n-C3H7ONO2 + h  products

## Primary photochemical transitions

| Reaction | H298/kJ·mol-1 | threshold/nm |
| --- | --- | --- |
| n-C3H7ONO2 + h  n-C3H7O + NO2 (1) | 165.9 | 721 |
|  C2H5CHO + HONO (2) | -92.8 |  |
|  C3H7ONO + O(3P) (3) |  |  |

Absorption cross-section data

| Wavelength range/nm | Reference | Comments |
| --- | --- | --- |
| 270-330 | Roberts and Fajer, 19891 | (a) |
| 185-330 | Turberg et al., 19902 | (b) |
| 220-340 | Clemitshaw et al., 19973 | (c) |

## Comments

(a)	Absorption cross-sections were measured in a cell of 10.2 cm pathlength using a single-beam spectrometer with a photometric accuracy of ±0.5%. No NO2 could be detected by FTIR in the n-propyl nitrate.

(b)	Absorption cross-sections were measured in 2 cm and 10 cm pathlength cells with a range of pressures of n-C3H7ONO2 at an unspecified spectral resolution.

(c)	Absorption cross-sections were measured with a dual-beam diode array spectrometer, with a spectral resolution of approximately 0.6 nm.  The purity of the n-propyl nitrate was checked by NMR and FTIR.

## Preferred Values

## Absorption cross-sections at 298 K

| /nm | 1020 /cm2 | /nm | 1020 /cm2 |
| --- | --- | --- | --- |
| 185 | 1810 | 265 | 3.6 |
| 190 | 1800 | 270 | 3.2 |
| 195 | 1600 | 275 | 2.8 |
| 200 | 1260 | 280 | 2.3 |
| 205 | 855 | 285 | 1.8 |
| 210 | 489 | 290 | 1.3 |
| 215 | 244 | 295 | 0.95 |
| 220 | 105 | 300 | 0.57 |
| 225 | 50 | 305 | 0.34 |
| 230 | 27 | 310 | 0.19 |
| 235 | 15 | 315 | 0.10 |
| 240 | 8.9 | 320 | 0.053 |
| 245 | 6.0 | 325 | 0.031 |
| 250 | 4.8 | 330 | 0.022 |
| 255 | 4.4 | 335 | 0.018 |
| 260 | 4.0 | 340 | 0.016 |

Comments on Preferred Values

Clemitshaw et al.3 have measured the absorption cross-sections at 298 K over the range 220 nm to 340 nm.  In the wavelength region where their measurements overlap with those of Roberts and Fajer1 (270 nm to 320 nm), the two studies are in excellent agreement.  Agreement with the results of Turberg et al.2 is also very good in the range 220 nm to 295 nm, but the results of Turberg et al.2 deviate significantly from those of both Clemitshaw et al.3 and Roberts and Fajer1 at  > 295 nm.  This tendency to obtain higher values than others of the absorption cross-section at longer wavelengths is noticeable in the results of Turberg et al.2 in all of their studies of the higher nitrates and could be due to traces of NO2 in their samples.

The preferred values of the absorption cross-section are those of Turberg et al.2 for the range 185 nm to 220 nm where theirs are the only measurements.  Over the range 220 nm to 295 nm averages are taken of the results of Roberts and Fajer,1 Turberg et al.2 and Clemitshaw et al.3 where their studies overlap, and over the range 295 nm to 340 nm the preferred values are based on the results of Roberts and Fajer1 and Clemitshaw et al.3

There are no data on either the products of photodissociation or the quantum yields.  However, the quantum yields for photodissociation of both ethyl and methyl nitrate to form NO2 have been shown to be unity at 308 nm and 248 nm, respectively (see data sheets in this evaluation). Since the absorption spectra of organic nitrates are very similar, with structureless continua occurring in the same region of the spectrum, it seems likely that the photodissociation quantum yield for n-propyl nitrate will also be unity. Further support for this conclusion comes from direct measurements4 of the rate of formation of NO2 from the photolyses of n-C3H7ONO2 in sunlight. These agreed well with the calculated rates of photolyses, based on measurements of the absorption cross-sections, solar irradiances, and an assumed value of 1 = 1 throughout the wavelength region 290 nm to 340 nm.4

## References

- J. M. Roberts and R. W. Fajer, Environ. Sci. Technol. 23, 945 (1989).

- M. P. Turberg, D. M. Giolando, C. Tilt, T. Soper, S. Mason, M. Davies, P. Klingensmith, and G. A. Takacs, J. Photochem. Photobiol. A51, 281 (1990).

- K. C. Clemitshaw, J. Williams, O. V. Rattigan, D. E. Shallcross, K. S. Law, and R. A. Cox, J. Photochem. Photobiol. A: Chemistry 102, 117 (1997).

- W. T. Luke, R. R. Dickerson, and L. J. Nunnermacker, J. Geophys. Res. 94, 14905 (1989).