# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet P25

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission. The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: June 2011; last change in preferred values: June 2011

CH3C(O)CH2OH + h  products

## Primary photochemical transitions

| Reaction | H298/kJ·mol-1 | threshold/nm |
| --- | --- | --- |
| CH3C(O)CH2OH  CH3C(O) + CH2OH (1) |  |  |
|  CH3 + HOCH2CO (2) |  |  |
|  C3H8 OH + CO (3) |  |  |

Absorption cross-section data

| Wavelength range/nm | Reference | Comments |
| --- | --- | --- |
| 207 - 333 | Mellor and Crowley, 1990 | (a) |
| 235 – 340 | Orlando et al. 1999 | (b) |
| 240 – 350 | Butovskaya et al., 2006 | (c) |
| 184.9 | Dillon et al., 2006 | (d) |

Quantum yield data ( = 1 + 2 + 3)

| Measurement | Wavelength range/nm | Reference | Comments |
| --- | --- | --- | --- |
|  = 0.65±0.25 (750 Torr air) | 240-420 | Orlando et al., 2006 | (e) |

## Comments

(a)	Cross-sections determined from absorption measurements as a function of CH3C(O)CH2OH pressure using a diode array spectrometer, with resolution of 0.25 nm.  These results are reported in the on-line Mainz Spectral Atlas (see http://www.atmosphere.mpg.de/enid/201aae7d473a97fc66e7686c134902ed,0/Spectra/Introduction_1rr.html)

(b)	Diode array spectrometer, with spectral resolution of the instrument about 0.6 nm.  UV absorption cross sections for hydroxyacetone measured over the wavelength range 235 to 340 nm; the spectrum is blue-shifted by about 15 nm relative to that of acetone and peaks at 266 nm, with a maximum absorption cross section of (6.7±0.x 10-20  cm2 molecule-1. Measurable absorption extends out to about 330 nm

(c)	Both absolute and relative mesurements of the cross section at 184.9 nm. In the absolute determination, i.e., measurement of the attenuation of 184.9 nm light by undiluted, static samples of hydroxyacetone at pressures of 0.28-0.501 Torr, a mean value of σ = (5.43 ± 0.08) x 10-18 cm2 molecule-1 was obtained. In the second experiment, measurement in a flowing system with the hydroxyacetone diluted in nitrogen relative to the spectrum of Orlando et al.,(2006) gave σ = (5.44 ± 0.02) cm2 molecule-1

(d)	The spectrum was measured by conventional diode array spectrometry in both static and flowing mixtures containing known concentrations of HAC. Measurements were performed at two temperatures: 294 and 328 K. The standard deviation was less than 5% over the wavelengths between 250 nm and 300 nm, and larger than 10% at wavelength greater than 300 nm.

(e)	Broad band steady-state photolysis of CH3C(O)CH2OH in the presence of air at 298 K.  Products measured by FTIR were CO, CH2O, CH3COOH, CH3COO2H, HCOOH and CH3OH. Average quantum yields of CH3C(O)CH2OH decay were measured for wavelength range 240 – 420 nm.

Preferred Values

## Absorption cross-sections at 298 K

| /nm | 1020/cm2 |  | 1020/cm2 | /nm | 1020/cm2 |
| --- | --- | --- | --- | --- | --- |
| 236 | 2.13 | 270 | 6.61 | 304 | 0.652 |
| 237 | 2.29 | 271 | 6.53 | 305 | 0.569 |
| 238 | 2.43 | 272 | 6.42 | 306 | 0.493 |
| 239 | 2.59 | 273 | 6.30 | 307 | 0.431 |
| 240 | 2.78 | 274 | 6.18 | 308 | 0.379 |
| 241 | 2.94 | 275 | 6.05 | 309 | 0.331 |
| 242 | 3.14 | 276 | 5.90 | 310 | 0.287 |
| 243 | 3.34 | 277 | 5.73 | 311 | 0.249 |
| 244 | 3.55 | 278 | 5.54 | 312 | 0.219 |
| 245 | 3.74 | 279 | 5.33 | 313 | 0.192 |
| 246 | 3.95 | 280 | 5.12 | 314 | 0.177 |
| 247 | 4.14 | 281 | 4.91 | 315 | 0.157 |
| 248 | 4.34 | 282 | 4.69 | 316 | 0.142 |
| 249 | 4.56 | 283 | 4.48 | 317 | 0.133 |
| 250 | 4.76 | 284 | 4.27 | 318 | 0.117 |
| 251 | 4.98 | 285 | 4.05 | 319 | 0.104 |
| 252 | 5.18 | 286 | 3.82 | 320 | 0.095 |
| 253 | 5.36 | 287 | 3.58 | 321 | 0.087 |
| 254 | 5.54 | 288 | 3.34 | 322 | 0.078 |
| 255 | 5.72 | 289 | 3.11 | 323 | 0.072 |
| 256 | 5.89 | 290 | 2.87 | 324 | 0.067 |
| 257 | 6.06 | 291 | 2.66 | 325 | 0.063 |
| 258 | 6.19 | 292 | 2.45 | 326 | 0.065 |
| 259 | 6.30 | 293 | 2.26 | 327 | 0.057 |
| 260 | 6.41 | 294 | 2.06 | 328 | 0.051 |
| 261 | 6.50 | 295 | 1.87 | 329 | 0.051 |
| 262 | 6.61 | 296 | 1.69 | 330 | 0.046 |
| 263 | 6.68 | 297 | 1.52 | 331 | 0.041 |
| 264 | 6.72 | 298 | 1.36 | 332 | 0.037 |
| 265 | 6.74 | 299 | 1.22 | 333 | 0.036 |
| 266 | 6.74 | 300 | 1.08 | 334 | 0.037 |
| 267 | 6.74 | 301 | 0.961 | 335 | 0.035 |
| 268 | 6.71 | 302 | 0.843 | 336 | 0.031 |
| 269 | 6.67 | 303 | 0.743 |  |  |

## Quantum Yields

 = 0.60 over the wavelength range 240 – 380 nm.

1 = 0.31 for 1 bar air,

Comments on Preferred Values

UV absorption spectrum of hydroxyacetone consists of a broad structureless band over the wavelength range 230 to 340 nm; the spectrum is blue-shifted by about 15 nm relative to that of acetone and peaks at 266 nm.  The three reported spectra show similar shape but the cross-sections at the maximum of absorption near 266 nm differ, covering the range 5.43 x 10-20 (Butkovskaya et al. 2006) to 6.74 x 10-20 cm2molecule-1 (Orlando et al, 1999). . Uncertainties (2s) in the cross sections reported by Orlando et al. are ~±10% near the peak of the spectrum and increase to about ±35% at the longest wavelengths measured. The errors are dominated by possible systematic errors associated with sample purity. Only experimental statistical errors were reported by Butkovskaya et al. and the results from the two methods did not agree very well. The JPL evaluation recommended a mean of the 3 cited studies, in the overlapping range.  However the excellent agreement between the absolute and relative determinations of s at 184.9nm of Dillon et al. (2006) provides an indirect confirmation of the UV spectrum reported by Orlando et al. (1999), and we recommend these cross sections.

The quantum yields from the same study of Orlando et al.(1999) are the only reported data, and form the basis of our recommendation for calculation of atmospheric photolysis rates.  The product analysis in that work suggest that <50% photodissociation proceeds via channel (1), and significant formation of HOCH2CO radicals.

#### References

N.I. Butkovskaya, N. Pouvesle, A. Kukui, Y. Mu, and G. Le Bras, , J. Phys. Chem. A 110, 6833-6843, 2006.

T.J. Dillon, A. Horowitz, D. Hölscher, J.N. Crowley, L. Vereecken, and J. Peeters, Phys. Chem. Chem. Phys. 8, 236-246 (2008).

R. Meller, J.N. Crowley, personal communication (1990) to

E.-P. Röth, R. Ruhnke, G. Moortgat, R. Meller, and W. Schneider, Berichte des Forschungszentums Jülich, jül-3341 (1997).

J.J. Orlando, G.S. Tyndall, J.-M. Fracheboud, E.G. Estupiñan, S. Haberkorn, and A. Zimmer, Atmos. Environ. 33, 1621-1629, 1999.