### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet P34

Datasheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission. The citation for the preferred values in this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This datasheet last evaluated: June 2015; last change in preferred values: June 2015.

CH3CHOO (syn and anti) + h  products

Primary photochemical transitions

| Reaction | H298/kJ·mol-1 | threshold/nm |
| --- | --- | --- |
| CH3CHOO + h  CH3CHO + O(3P) (1) | 185 | 645 |
|  CH3CHO + O(1D) (2) | 292 | 410 |

Absorption cross-section data

| Wavelength range/nm | Reference | Comments |
| --- | --- | --- |
| 280-410 | Beames et al., 2013 | (a) |
| 300-445 | Sheps et al., 2014 | (b) |
| 280-500 | Smith et al., 2014 | (c) |

Comments

(a)	CH3CHOO prepared by PLP (248 nm) of CH3CHI2 in O2/Ar mixtures in a capillary tube.  The photoproducts were cooled in a supersonic expansion and passed to a TOF mass spectrometer where they were ionised with VUV radiation at 118nm. The signal at m/z 46 detected when 248nm photolysis occurred in the capillary, was attributed to CH3CHOO. Both syn- and anti- conformers of the acetaldehyde oxide species were formed in the process. The UV absorption spectrum was determined from depletion of the m/z 46 photo-ionisation signal resulting from excitation of the B ( X transition in ground state CH3CHOO molecules by tunable UV radiation (280 – 420 nm) from a Nd-YAG laser. The UV-induced depletion approaches 100% near the peak of the simple Gaussian profile at 320 nm, indicating rapid dynamics in the B state, and corresponds to a peak absorption cross section of ~5 × 10−17 cm2 molecule−1; the absolute cross section measurements have an uncertainty on the order of a factor of 2. The electronic spectrum for CH3CHOO is similar to that reported recently for CH2OO, but shifted 15 nm to shorter wavelength.

(b)	CH3CHOO prepared by PLP (266 nm) of CH3CHI2 in O2/Ar mixtures at 5.1 Torr pressure. Absorption of CH3CHOO in the absence and presence of excess SO2 or H2O was observed by time-resolved UV absorption spectrum at 300 – 425 nm. Spectral resolution was ~1 nm. Absorption features due to the B ( X transition in ground state of syn and anti conformers of CH3CHOO could be distinguished by their differing reactivities - reflected in characteristic time dependencies for decay of these absorption features. The absorption band for the syn-CH3CHOO absorption band peaked at 323 nm, with a 40nm FWHM, and for the anti-CH3CHOO, FWHM was 35nm FWHM centred at 360 nm. Estimates of the absolute absorption cross sections of the two conformers was based on the value obtained by Smith et al (2014) , using the ion depletion method, for syn-CH3CHOO at 308 nm, where only the syn conformer absorbs.  The values obtained at the observed peaks of the syn-CH3CHOO absorption band, 323 nm, was σ = 1.2 x10−17 cm2, and for the peak anti-CH3CHOO absorption at 360 nm, was σ = 1.2 x10−17 cm2.

(c)	CH3CHOO was prepared by pulsed-248 nm photolysis of CH3CHI2/O2 mixtures. Transient absorption spectra were recorded using a gated iCCD spectrometer (1 ms gate width), after the probe light was dispersed using a grating monochromator. Spectral resolution was1.5nm, and up to 18 spectra were recorded at delay times up to 484 ms over the spectral range 260 – 500 nm. Decay of CH3CHOO by self-reaction and by reaction with SO2 were utilized to extract the absorption spectrum of CH2OO, corrected for contributions by other absorbers, under reaction conditions.  Absolute absorption cross-sections of CH3CHOO were obtained from laser-depletion measurements in a jet-cooled molecular beam (as described by Ting et al 2014 for CH2OO), using EI-MS to monitor C2H4OO+ at m/z = 60.  The laser fluence was calibrated with a reference molecule. The values obtained at 308 and 352 nm were: (1.06 ± 0.09) x 10-17 cm2 and (9.7 ± 0.0.6) x 10-17 cm2 respectively.  These values were consistent with the absorption measurements at these wavelengths and were used to calibrate the spectrum to provide absolute cross sections over the range 280 – 480 nm. The peak cross section is max = (1.27 ± 0.11) x 10-17 cm2 at 328 nm. The peak wavelength is blue shifted by 14 nm from the max for CH2OO at 342 nm.

Preferred Values

Absorption cross-sections at 298 K

| (/nm | /cm-2 x 10-20 | (/nm | /cm-2 x 10-20 | (/nm | /cm-2 x 10-20 |
| --- | --- | --- | --- | --- | --- |
| 280 | 190 | 340 | 1230 | 400 | 345 |
| 285 | 290 | 345 | 1215 | 405 | 190 |
| 290 | 380 | 350 | 1200 | 410 | 230 |
| 295 | 490 | 355 | 1125 | 415 | 110 |
| 300 | 551 | 360 | 1050 | 420 | 120 |
| 305 | 660 | 365 | 1004 | 425 | 45 |
| 310 | 785 | 370 | 844 | 430 | 50 |
| 315 | 920 | 375 | 767 | 435 | 30 |
| 320 | 979 | 380 | 720 | 440 | 0 |
| 325 | 1075 | 385 | 455 | 445 | 0 |
| 330 | 1140 | 390 | 520 | 450 | 0 |
| 335 | 1195 | 395 | 300 | 455 | 0 |

 = (1.23 ± 0.18) x 10-17 cm2  at max (340 nm) ;

Gaussian fit parameters to data of Smith et al. (2014):  = 1253.16 x exp(-0.000460967 x (328.28 - )2)

Absorption cross-sections at 298 K (conformer resolved)

| (/nm |  (syn) /cm-2 x 10-20 |  (anti) /cm-2 x 10-20 |
| --- | --- | --- |
| 300 | 847 | 209 |
| 310 | 1180 | 287 |
| 330 | 1150 | 913 |
| 350 | 906 | 1070 |
| 370 | 318 | 1200 |
| 390 | 59 | 965 |
| 410 | 12 | 652 |
| 430 | 0 | 210 |

 (syn) = (1.20 ± 0.18) x 10-17 cm2  at max (323 nm)

 (anti) = (1.20 ± 0.18) x 10-17 cm2  at max (360 nm)

Gaussian fit parameters to data for syn-CH3CHOO:  = 1253.18 x 10-20 exp(-0.00060787 x (324.11 - )2).

Gaussian fit parameters to data for anti-CH3CHOO:  = 1228.72 x 10-20 exp(-0.00037271 x (365.53 - )2)

Quantum Yields

1 = 1.0 for 280 <  > 420 nm.

Comments on Preferred Values

All reported studies of UV absorption by the acetaldehyde oxide Creigee diradical show a broad gaussian band peaking at about 320 nm with weak structure on the long-wavelength side, which is attributed to the in the B̃ (1A′) ← X̃(1A′) electronic transition. Generally the results from techniques using absorption spectroscopy (Sheps et al., 2013; Smith et al., 2014), and using the UV photo-dissociation action spectrum of CH3CHOO of Smith et al. (2014), are in good agreement on the overall shape of the spectrum. However the action spectrum reported by Beames et al, (2013) differs substantially from the other studies in that the band is narrower (FWHM = 37 nm vs 77 nm), and the peak cross section determined from photo-dissociation action spectrum at  = 320 nm is a factor of 4 higher than by Smith et al. (2014). Smith et al (2014) also used the photo-dissociation action technique with direct laser fluence measurements to give improved accuracy for (CH3CHOO) at 352nm and 308nm. They also measured the cross-section ratio (CH3CHOO)/(CH3CHI2) at 308nm, and determined (CH3CHOO) based the known value for (CH3CHI2) at this wavelength. These results agreed and were combined with multiplex long-path UV absorption to determine (CH3CHOO) over a wide range of wavelengths. These form the basis of the preferred cross sections in this evaluation.  The IUPAC recommended peak cross section at 340 nm and cross-sections at 5nm intervals are evaluated by averaging data from their analysis. Fig 1 shows the values reported by Smith et al and a Gaussian fit to these data. The error of ±15% includes possible variations arising from the temperature effects.

The source chemistry produces CH3CHOO in two (stable) conformers: syn- and anti- , which differ in the orientation of the O-O moiety relative to the CH3- group. Only the study of Sheps et al. (2104) provides cross sections for the individual conformers, by extracting their spectral contributions to the overall absorption band, using their different decay times (175 ± 25 and 2800 ± 300 s-1, for syn- and anti- CH3CHOO respectively ) in the presence of 1 x 1017 cm-3 [H2O].  The sum of absorption components for syn- and anti- CH3CHOO extrapolated to t = 0, agree well with the overall spectra reported by Smith et al. (2104), and are consistent with initial production of ~30% of total CH3CHOO in the anti-conformer. The IUPAC preferred cross sections at 5 nm intervals were calculated by averaging data from their experiments. Fig 2 shows a Gaussian fit to the retrieved conformer-resolved cross-sections. The error of ±30% on the conformer cross-sections arises mainly from the fitting procedure used to deconvolute the overlap of the conformer spectra.  The UV spectrum of syn- CH3CHOO is centred at 323nm and has FWHM of ~40 nm, whilst the peak cross section of the anti-conformer is ~360 nm. Both conformers have approximately equal cross-sections at the peak. The spectral features are consistent with theoretical calculations where a combination of ground state stabilization and excited state destabilization shifts the vertical B-X transition for syn-CH3CHOO (∼3.8 eV) to higher energy, and correspondingly shorter wavelength, than those for anti-CH3CHOO (∼3.5 eV) and CH2OO (∼3.6 eV), in each case starting from the equilibrium configuration.

The photodissociation quantum yields are likely to be close to unity.  Hydroxyl radicals produced concurrently with the generation of the Criegee intermediates were measured in the experiments of Beames et al, (2013), where they were detected by 1+1′ resonance enhanced multiphoton ionization. The OH yield observed with CH3CHOO is 4-fold larger than that from CH2OO, consistent with prior studies of OH generation from alkene ozonolysis.

References

Beames, J. M., Liu, Fang Lu, Lu Lu, and Lester, M. I.: J. Chem. Phys. 138, 244307, 2013.

Sheps, L., Scully, A.M. and Au, K., Phys.Chem.Chem.Phys.: 16, 26701, 2014.

Smith, M.C., Ting,W-L, Chang, C-H., Takahashi, K., Boering, K.A., and Lin, J. Jr -M.: J. Chem. Phys., 141, 074302, 2014.

Lehman, J.H., Li, H., Beames, J. M., and Lester, M. I.: J. Chem. Phys., 139, 141103, 2013

Figure 1:     Absorption spectrum of CH3CHOO, syn- and anti- conformers not resolved; Gaussian fit to experimental data (from Smith et al., 2014) shown as dotted line.

Figure 2	Absorption spectrum of CH3CHOO, syn- and anti- conformers resolved (shown as blue and black points, respectively); Gaussian fits to experimental data (from Sheps et al., 2014) shown as dotted line.