# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet PBr14

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission.

This data sheet updated: 15th December 2000.

CHBr3 + h  products

# Primary photochemical processes

| Reaction | H/kJ mol-1 | threshold/nm |
| --- | --- | --- |
| CHBr3 + h  CHBr2 + Br | 276 | 433 |

# Absorption cross-section data

| Wavelength range/nm | Reference | Comments |
| --- | --- | --- |
| 170-310 | Gillotay and Simon, 19891 | (a) |
| 286-362 | Moortgat, Meller, and Schneider, 19932 | (b) |

Quantum yield data

No experimental data are available.

# Comments

(a)	Two different techniques were used.  One employed a cell with a fixed optical path of 2 m and an evacuated monochromator capable of reaching wavelengths down to 170 nm.  In the other a multiple reflection cell with optical paths up to 5 m was used.  In both cases the cells were thermostatted and measurements were made in the range 295-240 K.

(b)	Measurements were made using two pieces of apparatus.  In one a cell of 63 cm fixed path length was used and measurements made at 296 K.  The other contained multiple pass optics with a total path length of 980 cm.  The latter system was used for measurements at 296 K, 286 K, 266 K, and 256 K.

# Preferred Values

Absorption cross-sections of CHBr3 at 296 K and 210 K.

| /nm | 1020 /cm2 | /nm | 1020 /cm2 |
| --- | --- | --- | --- |
|  | 296 K | 210 K |  | 296 K | 210 K |
| 190 | 399 | 393 | 270 | 30.8 | 21.1 |
| 192 | 360 | 351 | 272 | 24.8 | 16.5 |
| 194 | 351 | 353 | 274 | 19.8 | 12.8 |
| 196 | 366 | 383 | 276 | 15.8 | 9.94 |
| 198 | 393 | 422 | 278 | 12.5 | 7.66 |
| 200 | 416 | 466 | 280 | 9.88 | 5.88 |
| 202 | 433 | 475 | 282 | 7.77 | 4.50 |
| 204 | 440 | 474 | 284 | 6.10 | 3.42 |
| 206 | 445 | 467 | 286 | 4.81 | 2.60 |
| 208 | 451 | 471 | 288 | 3.75 | 1.97 |
| 210 | 468 | 490 | 290 | 2.88 | 1.49 |
| 212 | 493 | 522 | 292 | 2.22 | 1.05 |
| 214 | 524 | 551 | 294 | 1.70 | 0.757 |
| 216 | 553 | 593 | 296 | 1.28 | 0.547 |
| 218 | 574 | 621 | 298 | 0.951 | 0.395 |
| 220 | 582 | 633 | 300 | 0.719 | 0.285 |
| 222 | 578 | 623 | 302 | 0.530 | 0.206 |
| 224 | 558 | 597 | 304 | 0.394 | 0.149 |
| 226 | 527 | 562 | 306 | 0.298 | 0.107 |
| 228 | 487 | 516 | 308 | 0.226 | 0.078 |
| 230 | 441 | 465 | 310 | 0.171 | 0.060 |
| 232 | 397 | 409 | 312 | 0.127 | 0.040 |
| 234 | 362 | 362 | 314 | 0.095 | 0.029 |
| 236 | 324 | 324 | 316 | 0.071 | 0.021 |
| 238 | 295 | 295 | 318 | 0.053 | 0.015 |
| 240 | 273 | 272 | 320 | 0.039 | 0.011 |
| 242 | 253 | 250 | 322 | 0.029 | 0.0079 |
| 244 | 234 | 224 | 324 | 0.021 | 0.0057 |
| 246 | 214 | 202 | 326 | 0.016 | 0.0041 |
| 248 | 194 | 178 | 328 | 0.009 | 0.0030 |
| 250 | 174 | 157 | 330 | 0.009 | 0.0022 |
| 252 | 158 | 138 | 332 | 0.007 | 0.0016 |
| 254 | 136 | 116 | 334 | 0.005 | 0.0011 |
| 256 | 116 | 96.2 | 336 | 0.004 | 0.00081 |
| 258 | 98.6 | 79.5 | 338 | 0.003 | 0.00059 |
| 260 | 82.8 | 64.7 | 340 | 0.002 | 0.00042 |
| 262 | 68.9 | 52.5 |  |  |  |
| 264 | 56.9 | 42.2 |  |  |  |
| 266 | 46.7 | 33.7 |  |  |  |
| 268 | 38.0 | 26.7 |  |  |  |

## Comments on Preferred Values

There have been two studies of the absorption cross-sections of CHBr3.  Gillotay et al.1 reported values over the wavelength range 170-310 nm and the temperature range 295-240 K; Moortgat et al.2 reported values over the range 245-360 nm and the temperature range 296-256 K.  In the region where the measurements overlap, the agreement is very good.  The preferred values at 296 K are those reported by Gillotay et al.1 over the wavelength range 190-284 nm and those reported by Moortgat et al.2 at longer wavelengths.  The preferred values at 210 K are those of Gillotay et al.1 over the range 190-298 K, which they obtained by extrapolation of their higher temperature results, and those over the range 290-340 K are from the expression, ln (,T) = (0.0618350 – 0.000241014 )(273-T) – (2.37616 + 0.1475688 ), which was derived by Moortgat et al.2 from a fit to the combined data of their study and that of Gillotay et al.1  It is valid in the wavelength range 290-340 nm and the temperature range 300-210 K.

Photolysis is expected to occur with unit quantum efficiency by breaking of the C-Br bond to yield CHBr2 + Br.

# References

1	D. Gillotay, A. Jenouvrier, B. Coquart, M. F. Merrienne, and P. C. Simon, Planet. Space Sci. 37, 1127 (1989).

2	G. K. Moortgat, R. Meller, and W. Schneider, pp.359-369, in “The Tropospheric Chemistry of Ozone in the Polar Regions,” H. Niki and K. H. Becker, editors, NATO ASI Series, Volume 17, Springer-Verlag, Berlin, 1993.