# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet PCl3

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

This data sheet updated: 20th July 2006.

OClO + h  products

Primary photochemical processes

| Reaction | H/kJ·mol-1 | threshold/nm |
| --- | --- | --- |
| OClO + h  ClO + O(3P) (1) | 255 | 470 |
|  Cl + O2 (2) | 26 | 4540 |

Preferred Values

Absorption cross-sections of OClO at the band peaks at 204 K, 296 K and 378 K

| Band | /nm | 1020 /cm2 |
| --- | --- | --- |
|  |  | 204 K | 296 K | 378 K |
| a(0) | 475.53 |  | 13 |  |
| a(1) | 461.15 | 17 | 17 | 16 |
| a(2) | 446.41 | 94 | 69 | 57 |
| a(3) | 432.81 | 220 | 166 | 134 |
| a(4) | 420.58 | 393 | 304 | 250 |
| a(5) | 408.83 | 578 | 479 | 378 |
| a(6) | 397.76 | 821 | 670 | 547 |
| a(7) | 387.37 | 1046 | 844 | 698 |
| a(8) | 377.44 | 1212 | 992 | 808 |
| a(9) | 368.30 | 1365 | 1136 | 920 |
| a(10) | 359.73 | 1454 | 1219 | 984 |
| a(11) | 351.30 | 1531 | 1275 | 989 |
| a(12) | 343.44 | 1507 | 1230 | 938 |
| a(13) | 336.08 | 1441 | 1139 | 864 |
| a(14) | 329.22 | 1243 | 974 | 746 |
| a(15) | 322.78 | 1009 | 791 | 628 |
| a(16) | 317.21 | 771 | 618 | 516 |
| a(17) | 311.53 | 542 | 435 | 390 |
| a(18) | 305.99 | 393 | 312 | 291 |
| a(19) | 300.87 | 256 | 219 | 216 |
| a(20) | 296.42 | 190 | 160 | 167 |
| a(21) | 291.77 | 138 | 114 | 130 |
| a(22) | 287.80 | 105 | 86 | 105 |
| a(23) | 283.51 | 89 | 72 | 90 |
| a(24) | 279.64 | 73 | 60 | 79 |
| a(25) | 275.74 | 59 | 46 |  |
| a(26) | 272.93 | 53 | 33 |  |

Quantum yields for OClO photolysis at 298 K

1 = 1.0 over the wavelength range 270-480 nm.

2 <0.04 between 365 and 450 nm.

Comments on Preferred Values

The preferred values of the absorption cross-sections at the peak of the bands [a(0) to a(26)] at 204 K, 296 K, and 378 K are the values reported by Wahner et al. (1987). The bands become appreciably sharper with decreasing temperature (Wahner et al., 1987). However, the integrated band intensities remain constant for all bands between 204 K and 296 K, and, therefore, the solar photolysis rate is not expected to have a significant temperature dependence. Spectra have been obtained over a different temperature range (213-293 K) at higher resolution and, using Fourier transform methods, with better wavelength accuracy by Kromminga et al. (2003). In wavelength regions where data overlap, these is generally good agreement in the cross section, though Kromminga et al. (2003) note some wavelength inconsistencies, presumably errors in the wavelength calibration by Wahner et al. (1987). For this reason, the Kromminga et al. data may be more suited for retrieval of OClO concentrations from high resolution absorption measurements. Photoabsorption measurements of OClO over the wavelength range of 125 to 470 nm at 298 K have been carried out by Hubinger and Nee (1994). Absorption cross-sections as a function of vibrational excitation are reported.

The recommended quantum yield of unity for O-atom production is based on results reported by Colussi (1990), and results of earlier studies discussed by Watson (1977). Vaida and co-workers (Vaida et al., 1989; Ruehl et al., 1990) reported the detection of Cl atoms by resonance-enhanced multiphoton ionisation (REMPI) in the photoisomerization of OClO to ClOO followed by dissociation to Cl + O2. Bishenden et al. (1991), using REMPI detection of Cl atoms, report that the quantum yield for Cl atom formation near 360 nm is 0.15  0.10. In contrast, Lawrence et al. (1990), using a technique involving charge transfer excitation of Cl-Xe collision pairs as a sensitive probe of Cl atoms, determined that the quantum yield for Cl atom production in the 359-368 nm region is <510-4. In a molecular beam-photofragment study over the wavelength range 350-475 nm, Davis and Lee (1992) observed the dominant products to be ClO + O and also observed Cl atom yields reaching a maximum of 3.9% near 404 nm, decreasing to < 0.2% in the wavelength range 350-370 nm, in qualitative agreement with the results of Lawrence et al. (1990). More recent experiments of Davis and Lee (1996) show that the quantum yield for Cl + O2 production is 3.9  0.8% at 404 nm, decreasing at longer and shorter wavelengths, and the branching ratio between the channels (1) and (2) depends on the OClO excited state vibrational mode. Delmdahl et al. (1998) observed nascent Cl atom formation between 360 and 450 nm. A quantum yield less than 3.6% was determined between 365 and 450 nm. Below 365 nm Cl atom formation resulting from the photolysis of vibrationally excited ClO (  4) radicals was observed.

References

Bishenden, E., Haddock, J., and Donaldson, D. J.: J. Phys. Chem., 95, 2113, 1991.

Colussi, A. J.: J. Phys. Chem., 94, 8922, 1990.

Davis, H. F., and Lee, Y. T.: J. Phys. Chem., 96, 5681, 1992.

Davis, H. F., and Lee, Y. T.: J. Chem. Phys., 105, 8142, 1996.

Delmdahl, R. F., Ullrich, S., and Gericke, K.-H.: J. Phys. Chem. A, 102, 7680, 1998.

Hubinger, S. and Nee, J. B.: Chem. Phys., 181, 247, 1994.

Kromminga, H., Orphal, J., Spietz, P., Voigt, S., and Burrows, J. P.: J. Photchem. Photobiol. A 157, 149-160, 2003.

Lawrence, W. G., Clemitshaw, K. C., and Apkarian, V. A.: J. Geophys. Res., 95, 18591, 1990.

Rühl, E., Jefferson, A., and Vaida, V.: J. Phys. Chem., 94, 2990, 1990.

Vaida, V., Solomon, S., Richard, E. C., Rühl, E., and Jefferson, A.: Nature, 342, 405, 1989.

Wahner, A., Tyndall, G. S., and Ravishankara, A. R.: J. Phys. Chem., 91, 2734, 1987.

Watson, R. T.: J. Phys. Chem. Ref. Data, 6, 871, 1977.

# Text boxes

Absorption cross sections of OClO: The solid line from Wahner et al. (1987) at 296 K and resolution of 0.07 nm. The dotted line of Kromminga et al. (2003) at 293 K and 20 cm-1 resolution.