# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet PI3

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission.

This data sheet updated: 17th February 2004.

IO + h  products

Primary photochemical processes

| Reaction |  | H/kJ mol-1 | threshold/nm |
| --- | --- | --- | --- |
| IO+ h  I + O(3P) | (1) | 240 | 500 |
|  IO + O(1D) | (2) | 430 | 280 |

# Absorption cross-section data

| Wavelength range/nm | Reference | Comments |
| --- | --- | --- |
| 427.2 | Sander, 19861 | (a) |
| 340-450 | Laszlo, Kurylo, and Huie, 19952 | (b) |
| 340-480 | Harwood et al., 19973 | (c) |
| 345-465 | Atkinson, Hudgens, and Orr-Ewing, 19994 | (e) |
| 345-465 | Bloss et al., 20015 | (d) |

Quantum yield data

| Measurement | Wavelength/nm | Reference | Comments |
| --- | --- | --- | --- |
| 1 > 0.90±0.190.26 | 355 | Ingham et al., 20006 | (f) |

Comments

- Flash photolysis-absorption spectroscopy study. Cross-sections at the head of the 4-0 band at 427.2 nm were measured at six temperatures in the range 250 K to 373 K. A strong temperature dependence was observed at temperatures <315 K, with  increasing with decreasing temperature.

- Pulsed laser photolysis-absorption spectroscopy study. A cross-section of (427.2 nm) = (2.8  0.5) x 10-17 cm2 molecule-1 at 298 K was obtained, at a resolution of 0.3 nm.

- Pulsed laser photolysis-absorption spectroscopy study. Cross-sections of (427.2 nm) = (3.0  0.4) x 10-17 cm2 molecule-1 and (3.6  0.5) x 10-17 cm2 molecule-1 were reported for resolutions of 0.44 nm and 0.14 nm, respectively, at 298 K.

- Pulsed laser photolysis of N2O-CF3I mixtures. IO radicals were detected by time-resolved CCD measurements of the post-laser pulse mixtures in the range 340 nm to 470 nm. Cross-sections of (427.2 nm) = (1.9 ± 0.2) x 10-17 cm2 molecule-1 (resolution of 1.13 nm) and (395.5 nm) = (5.7 ± 0.5) x 10-18 cm2 molecule-1 were reported. They also reported a small temperature dependence of the cross-section at 427.2 nm, based on an analysis of the differential cross-section and taking into account the temperature and pressure dependence of the yield of IO radicals from the O(3P) + CF3I reaction.

- Pulsed laser photolysis of N2O-CF3I mixtures.  IO radicals were detected by time-resolved cavity ring-down spectroscopy (CRDS) at 445.40 nm (band head of rotationally resolved 2-0 band) and 455 nm (maximum of the diffuse 1-0) band).  Cross-sections of (445.40 nm) = (7.3 ± 0.7) x 10-17 cm2 molecule-1 and (455 nm) = (7.3 ± 0.8) x 10-18 cm2 molecule-1 were obtained using absolute value of 1.05 x 10-17 cm2 molecule-1 at 298 K obtained by Laslo et al2 for the 2-0 band head at a resolution of 0.3 nm.

- Pulsed laser photolysis (248 nm) of O3-I2 mixtures,  with photolysis of IO radicals by second laser pulse at 355 nm after a fixed time delay. O(3Pj) detected by time-resolved RF.  Quantum yield measured relative to NO2 photolysis at the same wavelength.

Preferred Values

Absorption cross-sections for IO at 298 K

| /nm | 1018 /cm2 | /nm | 1018 /cm2 |
| --- | --- | --- | --- |
| 345 | 0.78 | 410 | 7.53 |  |
| 350 | 1.00 | 415 | 5.18 |  |
| 355 | 1.36 | 420 | 9.04 |  |
| 360 | 1.85 | 425 | 4.17 |  |
| 365 | 2.25 | 430 | 6.11 |  |
| 370 | 2.99 | 435 | 6.92 |  |
| 375 | 3.57 | 440 | 1.61 |  |
| 380 | 4.42 | 445 | 4.94 |  |
| 385 | 4.63 | 450 | 1.02 |  |
| 390 | 5.65 | 455 | 2.36 |  |
| 395 | 6.55 | 460 | 0.90 |  |
| 400 | 6.40 | 465 | 0.39 |  |
| 405 | 7.09 |  |  |  |

Quantum Yields

(1) = 1.0 throughout the wavelength range 345 – 465 nm.

Comments on Preferred Values

Absorption Cross-Sections.  The measurements of the cross-sections at the band head of the 4-0 band at 427.2 nm by Laszlo et al.,2 Harwood et al.3 , Bloss et al.5 are in fairly good agreement when the effects of resolution are taken into account.  These data2-4 suggest a slightly higher value than the earlier data of Sander,1 Stickel et al.7 and Cox and Coker8 .  We recommend a value of (427.2 nm) = 3.6±0.3 x 10-17 cm2 molecule-1 based on the measurements of Harwood et al. 2 for the 4-0 band at high resolution (0.14 nm). The information from the studies of Harwood et al.3 and also of Hudgens et al4  at 298 K on the IO band shape and cross section at high resolution can be used to calculate the expected intensity and shape of the bands at lower resolution, which shows that the recent studies are consistent with this recommendation.

The study of Laszlo et al.2 showed that the vibronic band structure is superimposed on a broad continuous absorption which maximizes at ~400 nm.  Other recent studies3,5 confirm the presence of the underlying continuum, which makes a significant contribution to atmospheric photolysis.  Bloss et al.5 showed that IO absorption measurements in the 340 nm to 450 nm region can be influenced by the presence of an underlying absorption due to a product of the IO + IO reaction, and this was accounted for in their reported values for  in the continuum region5.  However Harwood et al. 2 observed the same decay kinetics when IO was monitored in the continuum region at 390 nm suggesting no interference due to product absorption. The agreement is good in thereported overall shape of the IO absorption envelope in the continuum between 350-400 nm where resolution is unimportant, from the three studies. The  absolute  cross sections reported by Bloss et al.5 in the continuum at 390 nm are a factor of 0.67 lower than those from Laszlo et al,2  and Harwood et al,3.   The preferred values for the IO cross-sections averaged over 5 nm intervals in the 345 nm to 465 nm are the values given by Bloss et al.5, scaled upwards by a factor of 1.5 to compensate for the lower resolution-independent value of (390 nm), obtained in this study.

The temperature dependence of (427.2 nm) has been investigated by Sander,1 Harwood et al.3 and Bloss et al.5.  The studies of Harwood et al.3 and Bloss et al.5 did not reproduce the large increase in  with decreasing temperature below 315 K observed by Sander,1 although values of  above 315 K are in good agreement.1,3,5 Bloss et al.5  found that the yield of IO from the O(3P) + CF3I reaction is apparently pressure and temperature dependent, and this was accounted for in deriving their expression for the small temperature dependence of (427.2 nm). Harwood et al.3 assumed a constant yield of IO from the O(3P) + CF3I reaction which resulted in a temperature-independent cross-section  at 427.2 nm.  Since the temperature dependence is clearly quite small, cross-sections in the banded region at low resolution can be assumed to be temperature independent.  Cross sections in the continuum region are assumed to be temperature and resolution independent.

Quantum Yields.  Turnipseed et al.9 observed LIF from the (0,0), (2,0), (3,0) and (2,1) bands of the A23/2X23/2 transition of IO.  The spectra are predissociated and the dissociation lifetime is <10 ns.10  The lifetime of the upper state of IO formed in the A-X transition is thus so short that quenching, fluorescence and processes other than dissociation by reaction (1) must be negligible,  and therefore the predominant fate of IO following light absorption is dissociation to O + I.  The measurement of Ingham et al.6 in the continuum at 355 nm confirms this conclusion for that region.

References

- S. P. Sander, J. Phys. Chem. 90, 2194 (1986).

- B. Laszlo, M. J. Kurylo and R. E. Huie, J. Phys. Chem. 99, 11701 (1995).

- M. H. Harwood, J. B. Burkholder, M. Hunter, R. W. Fox, and A. R. Ravishankara, J. Phys. Chem. A 101, 853 (1997).

- D . B. Atkinson, J. W. Hudgens, and A. J. Orr-Ewing, J. Phys. Chem. A 103, 6173 (1999).

- W .J. Bloss, D.M. Rowley, R.A. Cox, and R.L. Jones, J.Phys.Chem. A, 105, 7885, (2001).

- T. Ingham, M. Cameron amd J.N. Crowley, J.Phys.Chem.A, 104, 8001, (2000)

- R. E. Stickel, A. J. Hynes, J. D. Bradshaw, W. L. Chameides, and D. D. Davis, J. Phys. Chem. 92, 1862 (1988).

- R. A. Cox and G. B. Coker, J. Phys. Chem. 87, 4478 (1983).

- A. A. Turnipseed, M. K. Gilles, J. B. Burkholder, and A. R. Ravishankara, Chem. Phys. Lett. 242, 427 (1995).

- G. Inoue, M. Suzuki, and N. Washida, J. Chem. Phys. 79, 4730 (1983).