# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet PNOx7

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

This data sheet updated: 16th July 2001.

# N2O5 + h  products

# Primary photochemical transitions

| Reaction |  | H/kJ mol-1 | threshold/nm |
| --- | --- | --- | --- |
| N2O5 + h  NO3 + NO2 | (1) | 96 | 1252 |
|  NO3 + NO + O | (2) | 402 | 298 |
|  NO3 + NO2*  NO3 + NO2 + h | (3) |  |  |

# Absorption cross-section data

| Wavelength range/nm | Reference | Comments |
| --- | --- | --- |
| 200-380 | Yao, Wilson, and Johnston, 19841 | (a) |
| 240-420 | Harwood et al., 19932 | (b) |
| 208-398 | Harwood, Burkholder, and Ravishankara, 19983 | (c) |

#### Quantum yield data

| Measurement | Wavelength/nm | Reference | Comments |
| --- | --- | --- | --- |
| (NO3) | 249-350 | Swanson, Kan, and Johnston, 19824 | (d) |
| (NO3), [O(3P)] | 290 | Barker et al., 19855 | (e) |
| (NO3), [O(3P)] | 248-289 | Ravishankara et al., 19866 | (f) |
| (NO3) | 248, 308, 352.5 | Harwood, Burkholder, and Ravishankara, 19983 | (g) |

# Comments

(a)	Measured over the temperature range 223-300 K. For the wavelength range 200-280 nm, no temperature dependence was observed and values were tabulated at 5 nm intervals. For 285-385 nm, a pronounced temperature dependence was observed and the results were presented as an equation expressing  as a function of  and T.

- Measurements were made over the temperature range 233-313 K using a dual beam diode array spectrometer. Absolute cross-sections were based on pressure measurements and determination of NO2 and HNO3 impurities by spectroscopic methods. For 260-380 nm, a pronounced temperature dependence was observed and the results were expressed in the form log10() = A + B/T.

- Spectra were measured using a diode array spectrograph having a resolution of ~1 nm and were normalized to the value of  at 280 nm reported by Harwood et al.2  The N2O5 was analysed to check for HNO3 impurities and found to contain <1%.

- Pulsed laser photolysis, mostly at 249 nm, with a few experiments at 350 nm. The NO3 quantum yield was measured to be 0.890.15. At low reactant concentration, the quantum yield approached 1.00.1.

- Pulsed laser photolysis. The quantum yield for production of O(3P) atoms was determined to be < 0.1 in experiments with atomic resonance fluorescence detection of oxygen atoms. Optoacoustic techniques with added NO were used to determine (NO3) to be 0.80.2.

- Pulsed laser photolysis. The quantum yield for NO3 production at 249 nm was determined to be unity in experiments with detection of NO3 by absorption at 662 nm. The quantum yield for O(3P) production was observed to decrease from 0.720.17 at 248 nm to 0.150.05 at 289 nm.

- Pulsed laser photolysis at 248 nm, 308 nm, or 352.5 nm with [NO3] monitored by absorption at 661.9 nm. At each of the three photolysis wavelengths two different actinometric methods were used to establish the laser fluence for calculating the quantum yield. Values of (NO3) obtained were: at 248 nm (0.670.14, 0.640.08); at 308 nm (0.880.10, 1.030.10); at 352.5 nm (0.910.04, 1.210.04).  The quantum yields were independent of pressure over the range 197-789 mbar (150-600 Torr).

# Preferred Values

Absorption cross-sections of N2O5 at 298 K

| /nm | 1020/cm2 | B/K | /nm | 1020/cm2 | B/K |
| --- | --- | --- | --- | --- | --- |
| 210 | 470 |  | 315 | 1.62 | -0.253 |
| 215 | 316 |  | 320 | 1.21 | -0.294 |
| 220 | 193 |  | 325 | 0.89 | -0.338 |
| 225 | 128 |  | 330 | 0.67 | -0.388 |
| 230 | 91 |  | 335 | 0.50 | -0.409 |
| 235 | 73 |  | 340 | 0.38 | -0.492 |
| 240 | 60 |  | 345 | 0.279 | -0.530 |
| 245 | 51 |  | 350 | 0.215 | -0.583 |
| 250 | 40 |  | 355 | 0.164 | -0.719 |
| 255 | 32 |  | 360 | 0.124 | -0.770 |
| 260 | 25.9 | -0.091 | 365 | 0.091 | -0.801 |
| 265 | 20.4 | -0.100 | 370 | 0.072 | -0.885 |
| 270 | 16.4 | -0.104 | 375 | 0.053 | -0.765 |
| 275 | 13.2 | -0.112 | 380 | 0.041 | -0.992 |
| 280 | 11.1 | -0.112 | 385 | 0.032 | -0.992 |
| 285 | 8.59 | -0.126 | 390 | 0.0228 | -0.949 |
| 290 | 6.71 | -0.135 | 395 | 0.0171 | -0.845 |
| 295 | 5.11 | -0.152 | 400 | 0.0138 | -0.966 |
| 300 | 3.87 | -0.170 | 405 | 0.0103 | -1.00 |
| 305 | 2.91 | -0.194 | 410 | 0.0080 | -1.16 |
| 310 | 2.17 | -0.226 |  |  |  |

Temperature dependence: log10T (cm2 molecule-1) = log10298 + 1000B(1/T – 1/298).

# Quantum Yields at 298 K

| /nm |  (NO3) |  (O) |
| --- | --- | --- |
| 248 | 0.8 | 0.72 |
| 266 |  | 0.38 |
| 287 |  | 0.21 |
| 289 |  | 0.15 |
| 300 | 1.0 |  |
| 350 | 1.0 |  |

## Comments on Preferred Values

The absorption cross sections reported by Harwood et al.2 are in excellent agreement with the earlier data of Yao et al.1 and the more recent values obtained by Harwood et al.3 at wavelengths > 240 nm. At wavelengths shorter than 240 nm the values obtained by Harwood et al.3 are lower than those of Yao et al.,1 the divergence between the two studies increasing with decreasing wavelength, so that at 210 nm the absorption cross-section obtained by Yao et al.1 is ~ 50% greater than that of Harwood et al.3  The preferred values for the cross-sections at 298 K were obtained by averaging the values obtained by Yao et al.,1 Harwood et al.,2 and Harwood et al.3 for   240 nm and averaging those of Yao et al.1 and Harwood et al.3 in the range 210-240 nm.

The temperature dependences of the cross-sections measured by Harwood et al.2 agree well with the values obtained by Yao et al.1 except at the longer wavelengths where the results in the former study show a slightly larger dependence. Thus, using the expressions for the temperature dependence and the A values given in the two studies, the  values calculated at 380 nm differ by about 30%.  The preferred values of the temperature coefficients are taken from Harwood et al.2

The quantum yields for NO3 and O atom formation have been measured at a number of wavelengths in the range 248-352.5 nm. The preferred value of (NO3) =1.0 at 300 nm and 350 nm are based on the results of Swanson et al.4 at 350 nm, Barker et al.5 at 290 nm, and Harwood et al.3 at 308 nm and 352.5 nm, which agree within the fairly substantial error limits. The value of (NO3) at wavelengths below 300 nm is less certain. A quantum yield close to unity has been reported by Swanson et al.4 at 249 nm and by Ravishankara et al.6 over the range 248-289 nm, but the recent study of Harwood et al.3 suggests a substantially lower value at 248 nm. Our preferred value of 0.8, with suggested error limits of at least 10%, reflects the findings of all of these studies.3,4,6

The preferred quantum yields for O atom production are those reported by Ravishankara et al.6 Barker et al.5 also report a quantum yield for O atom production of  < 0.1 at 290 nm in agreement with the findings of Ravishankara et al.6 that (O) is substantial at 248 nm but decreases with increasing wavelength, approaching zero in the neighbourhood of the thermodynamic threshold for O atom production at 298 nm.

The study of Oh et al.7 indicates that electronically excited NO2 in the 2B1 state is produced, and photolysis induced fluorescence (PIF) quantum yield values are reported.

# References

1	F. Yao, I. Wilson, and H. S. Johnston, J. Phys. Chem. 86, 3611 (1982).

2	M. H. Harwood, R. L. Jones, R. A. Cox, E. Lutman, and O. V. Rattigan, J. Photochem. Photobiol. A 73, 167 (1993).

3	M. H. Harwood, J. B. Burkholder, and A. R. Ravishankara, J. Phys. Chem. A 102, 1309 (1998).

4	D. Swanson, B. Kan, and H. S. Johnston, J. Phys. Chem. 88, 3115 (1984).

5	J. R. Barker, J. Brouwer, R. Patrick, M. J. Rossi, P. L. Trevor, and D. M. Golden, Int. J. Chem. Kinet. 17, 991 (1985).

6	A. R. Ravishankara, P. H. Wine, C. A. Smith, P. E. Barbone, and A. Torabi, J. Geophys. Res. 91, 5355 (1986).

7	D. Oh, W. Sisk, A. Young, and H. S. Johnston, J. Chem. Phys. 85, 7146 (1986).