Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet II.A6.128 ROO_9

Data sheets can be downloaded for personal use only and must not be re-transmitted or disseminated either electronically or in hard copy without explicit written permission. The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, (http://iupac.pole-ether.fr). This data sheet last evaluated: 4th June 2009. Last change in preferred values: 12th June 2003.

CH3O2 + NO2 +M  CH3O2NO2 + M

H° = -92.7 kJ·mol-1

Low-pressure rate coefficients

Rate coefficient data

| k0/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| (2.33 ± 0.08) x 10-30 [N2] | 298 | Sander and Watson, 19801 | FP-AS (a) |
| 2.2 x 10-30 (T/300)-2.5 [N2] | 253-353 | Ravishankara, Eisele, and Wine, 19802 | FP-AS (b) |
| (1.46  0.50) x 10-30 [SF6] | 295 | Wallington, Nielsen, and Sehested, 19993 | (c) |

## Comments

(a)	Pressure range 70 mbar to 900 mbar for the bath gases He, N2, and SF6. Analysis of the falloff curve was carried out with a theoretical Fc value of 0.39, in good agreement with the fitted value of Fc = 0.4 ± 0.10.

(b)	Pressure range 100 mbar to 950 mbar. Analyses of the falloff curves at 253 K, 298 K and 353 K were carried out with Fc = 0.4 independent of temperature.

(c)	Pulse radiolysis study in 0.5-14 bar of SF6. Evaluating of the falloff curve with Fc = 0.40.

Preferred Values

k0 = 2.5 x 10-30 (T/300)-5.5 [N2] cm3 molecule-1 s-1, over the temperature range 250 to 350 K.

Reliability

log k0 = ± 0.3 at 298 K.

n = ± 1.

Comments on Preferred Values

The preferred values are based on the results from refs. 1 and the theoretical analysis from ref. 4. These values are based on a theoretically determined value of Fc = 0.36 at 300 K.

### High-pressure rate coefficients

Rate coefficient data

| k/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| (8.0 ± 1.0) x 10 -12 | 298 | Sander and Watson, 19801 | FP-AS (a) |
| 7 x 10-12 (T/298) -3.5 | 253-353 | Ravishankara, Eisele, and Wine, 19802 | FP-AS (b) |
| (1.8  0.25) x 10-11 | 295 | Wallington, Nielsen, and Sehested, 19993 | (c) |

Comments

(a)	See comment (a) for k0.

(b)	See comment (b) for k0. The large negative temperature coefficient is probably an artifact of the interpretation. If a larger negative temperature exponent for k0 and a smaller Fc value at higher temperature are used, the large negative temperature exponent of k will decrease.

(c)	See comment (c) for k0.

Preferred Values

k = 4.0 x 10-12 cm3 molecule-1 s-1 at 298 K and 1 bar of air.

k = 1.8 x 10-11 cm3 molecule-1 s-1, independent of temperature over the range 250 to 350 K.

Reliability

log k =  0.3 at 298 K.

n = ± 0.5.

Comments on Preferred Values

The preferred values are based on the high pressure study from ref. 3. An experimental value of Fc = 0.36 at 298 K appears well established. Less complete information on the falloff range is obtained from the experiments by Cox and Tyndall,5 who measured k = 1.6 x 10-12 cm3 molecule-1 s-1 at 700 mbar of N2 and 1.2 x 10-12 cm3 molecule-1 s-1 at 66 mbar of Ar at 275 K, and Bridier, Lesclaux, and Veyret6 who measured k = 4.4 ( 0.4) x 10-12 cm3 molecule-1 s-1 at 298 K in 1 bar of air. The apparent observation of a pressure independent rate coefficient k over the range 66 mbar to 760 mbar of Ar, reported by Adachi and Basco,7 is not confirmed by refs. 1 and 2. H is taken from the equilibrium measurements of ref. 6.

The following text-line combines the preferred values for the high and low pressure limiting rate coefficients to generate a single, cut-and-paste expression for calculation of k:

=((2.5e-30*(T/300)^-5.5)*M*(1.8e-11))/((2.5e-30*(T/300)^-5.5)*M+(1.8e-11))*10^(log10(0.36)/(1+(log10((2.5e-30*(T/300)^-5.5)*M/(1.8e-11))/(0.75-1.27*log10(0.36)))^2))

The molecular density, M = 7.2431021P(bar)/T(K)

References

- S. P. Sander and R. T. Watson, J. Phys. Chem. 84, 1664 (1980).

- A. R. Ravishankara, F. L. Eisele, and P. H. Wine, J. Chem. Phys. 73, 3743 (1980).

- T. J. Wallington, O. J. Nielsen, and K. Sehested, Chem. Phys. Lett. 313, 456 (1999).

- M. Destriau and J. Troe, Int. J. Chem. Kinet. 22, 915 (1990).

- R. A. Cox and G. S. Tyndall, J. Chem. Soc. Faraday Trans. 2, 76, 153 (1980).

- I. Bridier, R. Lesclaux, and B. Veyret, Chem. Phys. Lett. 119, 259 (1992).

- H. Adachi and N. Basco, Int. J. Chem. Kinet. 12, 1 (1980).