### IUPAC Task Group on Atmospheric chemical Kinetic Data Evaluation – Data Sheet V.A1.53 HI53

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This data sheet last evaluated: June 2009; last change in preferred values: June 2009.

SO2 + H2O2-doped ice

# Experimental data

| Parameter | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Experimental uptake coefficients: (SO2) |  |  |  |
| (0.7-5.3) x 10-4 (3.0 wt % H2O2-ice film) | 191 | Chu et al. 2000 | CWFT-MS (a) |
| ~8.3 x 10-5 (3.0 wt % H2O2-ice film) | 211 |  |  |
| (0.1-1.0) x 10-5 (0.8 wt % H2O2-ice film) | 191 |  |  |
| (SO2) = (0.9-9.0) x 10-3 for P(SO2) fixed at 1.5 x 10-6 mbar and P(H2O2) = 2 x 10-5-2.5 x 10-4 mbar | 228 | Clegg and Abbatt, 2001 (b) | CWFT-MS (b) |
| (SO2) = (30 - 1.0) x 10-3 for P(H2O2) fixed at 8.7 x 10-5 mbar and P(SO2) = (0.3 - 20) x 10-6 mbar | 228 |  |  |

Comments

(a)	H2O2 doped ice surfaces were prepared by bubbling helium through H2O2 solutions (30 wt % or 3 wt %) into a flow tube at 190-211 K via a sliding injector. The resulting vapour deposited ice films were determined to contain 3 wt % and 0.8 wt % H2O2, respectively. The average film thickness was estimated to be ~2.5 µm. The SO2 partial pressure ranged from 1.6 x 10-5 to 5.1 x 10-5 mbar for uptake experiments on water-ice. The initial uptake coefficients, ,were corrected for axial and laminar diffusion. Corrections for surface roughness were performed using a layered pore diffusion model; giving the "true" value for the uptake coefficient, t, which are cited. These uptake coefficients decreased slightly with increasing SO2 partial pressure at 191 K, and were constant at 211 K. The surface coverage of SO2 on the 3.0 wt % H2O2 ice film ranged from 7 x 1013 to 4.7 x 1015 molecules/cm2 as the temperature increased from 191 to 211 K at a constant SO2 partial pressure of 1.7 x 10-6 mbar. It was shown by analysis of the exposed films by IC that SO2 was converted to sulphate upon uptake into H2O2 -doped films.

(b)	water-ice films were made by freezing a water-coated pyrex sleeve within the flow tube. Doped ice surfaces were prepared by flowing H2O2 over the ice film from the back of the flow tube until the entire length of the film surface was at equilibrium with the gaseous H2O2. A moveable sliding injector containing SO2 was pulled back in stages over the ice film. The SO2 and H2O2 partial pressure ranges are given in the table and in all cases, the H2O2 was the excess reagent. SO2 uptake on H2O2-doped ice films was much larger than on pure ice and was irreversible. For a fixed SO2 partial pressure of 1.5 x 10-6 mbar, the SO2 reaction probability varied linearly with the H2O2 partial pressure up to 3 x 10-4 mbar. For a fixed H2O2 partial pressure of 8.7 x 10-5 mbar, the SO2 reaction probability decreased with  p(SO2)~0.7 in the range (0.27 to 17) x 10-5 mbar

# Preferred Values

| Parameter | Value | T/K |
| --- | --- | --- |
| ks / cm2 molecule-1 s-1 | 4 x 10-12 | 228 |
| ks KlinC (SO2) /cm3molecule-1 s-1 | 2.9 x 10-15exp(2065/T) | 200- 230 |
| KlinC (H2O2) /cm | 1.6 | 228 |
| Nmax / molecule cm-2 | 3 x 1014 |  |

Reliability

|  log (ks KlinC (SO2)) | ± 0.3 | 228 |
| --- | --- | --- |
|  (E/R) /K | ± 1000 | 200-298 |

Comments on preferred values

Both Chu et al. (2000) and Clegg and Abbatt (2001) observed that the SO2 uptake is significantly enhanced by the presence of adsorbed H2O2. Unlike the reversible SO2 uptake observed on pure water-ice, the uptake on H2O2-doped ice is irreversible. This is due to the reaction of between H2O2 and SO2 forming sulfates on the ice surface (Chu et al., 2000). However SO2 loss rate was still time-dependent, declining as the surface was exposed. This was attributed to accumulation of H2SO4 products on the ice surface, which inhibits SO2 uptake. (see SO2 + ice data sheet, IUPAC 2009). This is as observed in some of the Chu et al. (2000) experiments, but the dependence of g on the SO2 partial pressure is stronger and better defined in the experiments of Clegg and Abbatt (2001). Note that a direct comparison between the experimental results of Chu et al. (2000) and those of Clegg and Abbatt (2001) is difficult as H2O2 surface coverages were uncertain in the experiments of Chu et al. (2000) who used frozen solutions of H2O2.

Clegg and Abbatt (2001) suggested the following mechanism to explain their observations:

| H2O2 (g)  H2O2 (ads) | (1) |
| --- | --- |
| SO2 (g)  SO2 (ads) | (2) |
| SO2 (ads) + H2O  H+(ads) + HSO3-(ads) | (3) |
| HSO3-(ads) + H2O2 (ads)  HOOSO2- (ads) + H2O | (4) |
| HOOSO2- (ads) + H+(ads)  2 H+(ads) + SO42-(ads) | (5) |

Eqn (4) is considered to be the rate-determining step. The overall rate of reaction is then proportional to ., noting the square root dependence of the SO2 surface coverage on the SO2 partial pressure (see SO2 + ice data sheet, IUPAC 2007), and the linear dependence on H2O2 coverage at low . In terms of the reaction probability for SO2, (SO2)  ..

However at low [SO2], surface coverage of SO2 on ice was approximately proportional to , although the SO2 reaction probability decreased with  p(SO2)~0.7 at fixed H2O2 coverage, indicating complexity in the chemistry.  For this evaluation we adopt a simple Langmuir-Hinshelwood formalism, with the uptake coefficient LH given by:

with

An average value for the parameter ks = 4 x 10-12 cm2molecule-1s-1  at 288 K was evaluated from the experimental [H2O2] dependence of gmeasured by Clegg and Abbatt (2001) on neutral (pH =6) ice, together with the IUPAC recommended value of KLinC(SO2) (see SO2 + ice data sheet, IUPAC 2009). This forms the basis of our recommendation, which should be applied only for SO2 partial pressures below ~1 x 10-6 mbar.  At higher SO2 the following [SO2] dependent expression for gLH gives a better description of the uptake rates:

where K(SO2) is given in the SO2+ice data sheet ( IUPAC 2009)

The strong influence of pH suggests that as H2SO4 builds up with each exposure of SO2 to the H2O2-doped surfaces, the surface protons inhibit reaction 3, the dissociation of SO2. This leads to less gas-phase SO2 adsorbing to the ice surface and hence a lower reaction probability. Clegg and Abbatt (2001) estimate that about 1014-1015 molecules/cm2 (i.e approx 1 ML) of H2SO4 need to be formed before the SO2 + H2O2  H2SO4 reaction shuts off (i.e., before the surface becomes poisoned with protons).

References

Chu, L., Diao, G. and Chu, L.T.: J. Phys. Chem. A 104, 7565 (2000).

Clegg, S. M and Abbatt, J. P. D.: Atmos Chem. Phys. 1, 73 (2001).

SO2 + ice datasheet, IUPAC 2007