### IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet V.A1.15 HI15

Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission.

The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, http://iupac.pole-ether.fr.

This Data sheet last evaluated: June 2009; last change in preferred values: June 2009.

SO2 + ice

# Experimental data

| Parameter | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Experimental uptake coefficients: 0, t |  |  |  |
| 0 = (0.8-3.0) x 10-5 | 191 | Chu et al. 2000 (a) | CWFT-MS (a) |
| t = (0.4-1.4) x 10-6 | 213-238 | Clegg and Abbatt, 2001 (b) | CWFT-MS (b) |
| Partition coefficient: KlinC(cm) |  |  |  |
| 36.5 ([SO2] = 6.6 x 1010 cm-3) | 191 | Chu et al. 2000 (a) | CWFT-MS (a) |
| 5.5 ( pH=6; [SO2] = 1.3 x 1010 cm-3) 7.1 ( pH=6; [SO2] = 4.2 x 1010 cm-3) 1.2 ( pH=6; [SO2] = 4.2 x 1012 cm-3) 0.47 ( pH=4.1; [SO2] = 4.2 x 1010 cm-3) 333 ( pH=10.4; [SO2] =2.1 x 1010 cm-3) | 228 | Clegg and Abbatt, 2001 (b) | CWFT-MS (b) |

Comments

(a)	Ice films were formed by vapour-deposition at 190-211 K with a thickness of ~2.5-3.0 m. The SO2 partial pressure ranged from 1.0 x10-6 to 2.3 x10-5 mbar. The initial uptake coefficients, ,were corrected for axial and laminar diffusion. Corrections for surface roughness were performed using a layered pore diffusion model; giving the "true" value for the uptake coefficient, t. The variability in the reported  values is due to a three-fold change in the SO2 partial pressure and variability in the surface area and roughness of the vapour-deposited water-ice films. On exposure the surfaces were rapidly saturated, and a single measurement reported a surface coverage of   = 2.4 x 1012 molecules/cm2 for = 1.0 x10-6 mbar at 191 K. These data were used to evaluate the cited value of KLinC.

(b)	Ice films made by freezing a water-coated pyrex sleeve within the flow tube. The SO2 partial pressure ranged from 3 x10-7 to 1.7 x10-4 mbar. The uptake saturated rapidly at a given SO2 partial pressure and surface coverage on pure ice over the whole range varies approximately with . The coverage,  was much less than a monolayer (Nmax was estimated to be 5 x 1014 molecules/cm2 for the ice surfaces prepared in this way) and shows a strong decrease with decreasing pH. The number of molecules desorbed from the ice surface was about equal to the number of molecules adsorbed, indicating that the adsorption process is fully reversible. The partition constants cited in the table were evaluated from surface coverages at selected  given in Figure 4 of Clegg and Abbatt’s paper, with emphasis on at the lower concentrations (<1.3 x 10-6 mbar) where  was approximately proportional to .

Preferred values

| Parameter | Value | T/K |
| --- | --- | --- |
| KlinC / cm | 6.3 | 228 |
| KlinC / cm | 7.3 x 10-4 exp(2065/T) | 190-250 |

Reliability

|  (lnKlinC) | ± 0.3 | 228 |
| --- | --- | --- |
|  (E/R) /K | ± 1000 | 190-250 |

Nads / molecule cm-2 = KlinC[SO2]

Comments on Preferred values

Chu et al. (2000) determined the initial SO2 uptake coefficient to be ~1 x 10-5 on water-ice films at 191 K but they did not observe the reversible uptake reported by Clegg and Abbatt (2001).  The weak reversible adsorption does not allow accurate determination of uptake coefficients and no recommendation is made for .

Clegg and Abbatt (2001) suggest that their observed dependence of the uptake on the [SO2]0.5 is due to dissociation of the hydrated form of SO2 to HSO3- on the ice surface. This was tested by raising and lowering the pH of their ice surfaces. It was found that SO2 uptake was enhanced at higher pH and was inhibited at lower pH (due to surface protons inhibiting the dissociation of adsorbed SO2). A simple precursor model was developed by Clegg and Abbatt (2001) to explain the observed SO2 uptake behaviour. The total adsorbed S(IV) tot (= [SO2]ads + [HSO3-]ads) at equilibrium is given as a function of [SO2]g by the expression: [S(IV)tot]ads = K1[SO2] + (K1K2[SO2])0.5. For ice at natural pH (~ 6) the experimental data at 228 K for [SO2]  in the range 1011 - 1013 molecule cm-3 were approximated by the expression: [S(IV)tot]ads = K[SO2]0.5 , where K = 1.2 x 106 molecule1/2 cm-1/2, indicating [HSO3-] is the predominant adsorbed species. This model is also consistent with up linear dependence on [SO2] at low and KlinC can be identified with K1[SO2]. The recommended partition coefficient at 228K  was evaluated from data of Clegg and Abbatt for SO2 on ice at partial pressures ≤1.3 x 10-6 mbar ([SO2] ≤ 1 x 1013 molecule cm-3).

Chu et al. reported a single measurement of partitioning to pure ice at 191 K, from which a value of KLinC = 36.5 cm can be derived, assuming this reflects linear dependence on [SO2].  This is substantially higher than the value at 228 K, which suggests a negative T dependence as expected for reversible adsorption. An Arrhenius fit to the data points at 191 and 228 K yields the recommended expression for the temperature dependence of KlinC.

Some support for the negative temperature dependence comes from the thesis work of  Langenberg (1997) who derived  DHads = -21±3 kJmol-1 and DSads = 39±10 Jmol-1K-1 from uptake of SO2 on a packed column over the temperature range  207 - 267 K. These results yield an expression for KlinC = 6.4 x 10-6 exp(2527/T) cm, and a value of 0.42 cm at 228, somewhat lower than the preferred value obtained by Clegg and Abbatt on ice at pH=6.

Clegg and Abbatt (2001) observed an increase in the surface coverage as the temperature was increased from 213 K to 228 K at a constantof 4 x 10-5 mbar (corresponding to a surface coverage of 1.5 x 1012 cm-2 at 228 K).  An Arrhenius fit to these data is consistent with earlier partitioning data for SO2 to ice (Clapsaddle and Lamb,1989) and gives the expression: [S(IV)tot]ads = {5.6 x 1012 exp(-4425/T)}x[SO2]0.5 molecule1/2 cm-1/2. It was suggested that the increase in surface coverage with temperature is due to the existence of a quasi-liquid layer on the ice surface, which increases in thickness and facilitates the dissociation of SO2 or can accommodate more S(IV) species, as temperature increases. However Huthwelker et al., (2001) showed, on the basis of a detailed analysis of uptake rates, amounts, and temperature dependence reported from earlier experimental data (Clapsaddle and Lamb, 1989; Conklin et al. 1989), that SO2 dissociates and diffuses into an internal reservoir for example comprised of veins and nodes, but not into a quasi-liquid layer on the ice surface.

References

Chu, L., Diao, G., and Chu, L. T.: J. Phys. Chem. A, 104, 7565, 2000.

Clegg, S. M., and Abbatt, J. P. D.: J. Phys. Chem. A, 105, 6630, 2001.

Clapsaddle, C., and Lamb, D.: Geophys. Res. Lett., 16, 1173, 1989.

Conklin, M. H., Laird, K., Sommerfeld, R. A., and Villinski, J. E.:  Atmos. Environ.A , 27, 159–166, 1993.

Langenberg, S., PhD thesis: Anwendung de Kapillar-Gaschromatographie zur Untersuchung von Spurengas-Aerosolwechselwirkungen, University of Bonn, Germany, 1997.

Th. Huthwelker, D. Lamb, Marcia Baker, B. Swanson and Th. Peter J. Colloid and Interface Science: 238, 147–159, 2001.