IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet SOx61

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hardcopy without explicit written permission.

This data sheet updated: 4th October 2006.

CH3SO + O3  products

## Rate coefficient data

| k/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| 1 x 10-12 | 298 | Tyndall and Ravishankara, 1989 | PLP-LIF |
| (6.0 ± 3.0) x 10-13 | 300 | Dominé et al., 1992 | (a) |
| Relative Rate Coefficients |  |  |  |
| (3.2 ± 1.6) x 10-13 | 300 | Borissenko et al., 2003 | (b) |

## Comments

(a)	Discharge flow study.  Photoionization mass spectrometry was used to monitor CH3SO radicals.  The reaction of O(3P) + C2H5SCH3 was used as a source of CH3SO radicals.  The reaction system is complex owing to chain branching processes and HO formation from unknown sources, the latter of which has been quenched by addition of 1.3x1014 molecule cm-3 of C2F3Cl.  The rate coefficient obtained was considered preliminary in view of the small number of experiments.

(b)	PLP/LIF study using LIF detection of the product SO2 excited at 220.6 nm into the short-lived C(tilde)(1B2) electronic state.  CH3SO was generated in the reaction O(3P) + CH3SCH3 (DMS) with O(3P) from O3 photolysis at 248 nm.  Relative SO2 yields from photolyzed mixtures of DMS/NO2/O3 were measured as a function of [O3]/[NO2] and resulted in the ratio k/kref(CH3SO + NO2 → products) = (2.13 ± 0.9) x 10-2.  This ratio was converted to k using kref(CH3SO + NO2 → products) = (1.5 ± 0.4) x 10-11 cm3 molecule-1s-1.  The absolute SO2 product yield was measured relative to the one from the photolysis of CH3SSCH3 (DMDS)/NO2 and CS2/NO2 mixtures resulting in SO2.  The SO2 yield of the CS2/NO2 photolysis system was assumed to be unity which allowed the measurement of absolute SO2 yields.  The study was performed over the pressure range 187-880 mbar of N2 and the SO2 yield, thus the branching ratio, was (1.0 ± 0.12) in the pressure range 667-933 mbar.

## Preferred Values

k = 4.1 x 10-13 cm3 molecule-1 s-1 at 298 K.

Reliability

log k = ± 0.15 at 298 K.

Comments on Preferred Values

The measurement of k by Dominé et al. (1992) is more direct than the original study of Tyndall and Ravishankara (1989) in which the rate coefficient was derived by a complex analysis of the reaction system.  However, there are still a number of uncertainties in the study by Dominé et al. (1992), who consider their quoted value of k to be preliminary.  The study by Borissenko et al. (2003) is a relative rate study based on CH3SO + NO2 that was also investigated by Kukui et al. (2000).  The branching ratio for the SO2-forming reaction channel as well as the relative rate constant have been obtained relative to the reference reaction CH3SO + NO2 over a comparable pressure range.  The branching ratio for SO2 formation in CH3SO + NO2 obtained by Borissenko et al. (2003) is a factor of two larger across the studied pressure range compared to the earlier study by Kukui et al. (2000) which, however, does not directly affect k.  Owing to the fact that the value of k by Borissenko et al. (2003) is within the uncertainty limit obtained by Dominé et al. (1992) the upper limiting k value of the latter is recommended because the pressure range extends to 880 mbar.

## References

Borissenko, D., Kukui, A., Laverdet, G. and Le Bras, G.: J. Phys. Chem. 107A, 1155, 2003.

Dominé, F., Ravishankara, A. R. and Howard, C. J.: J. Phys. Chem. 96, 2171, 1992.

Kukui, A., Bossoutrot, V., Laverdet, G. and Le Bras, G.: J. Phys. Chem. A 104, 935, 2000.

Tyndall, G. S. and Ravishankara, A. R.: J. Phys. Chem. 93, 2426, 1989.