# IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet II.A7.167 X_VOC3

Website: http://iupac.pole-ether.fr. See website for latest evaluated data. Data sheets can be downloaded for personal use only and must not be retransmitted or disseminated either electronically or in hard copy without explicit written permission. The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, (http://iupac.pole-ether.fr).

This data sheet last evaluated: June 2003.

Cl + C2H2 + M  C2H2Cl + M

Low-pressure rate coefficients

Rate coefficient data

| k0/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| (3.15 ± 0.30) x 10-21 T -3.5 [Ar] | 210-361 | Brunning and Stief, 19851 | FP-RF (a) |  |
| 6.9 x 10-30 [Ar] | 298 |  |  |  |
| Relative Rate Coefficients |  |  |  |  |
| (5.2 ± 0.7) x 10-30 [air] | 295 | Wallington et al., 19902 | (b) |  |
| 5.4 x 10-30 (T/300)-2.092 [air] | 252-370 | Kaiser, 19923 | (c) |  |
| (6.1 ± 0.2) x 10-30 [air] | 297 | Kaiser and Wallington, 19964 | (d) |  |

Comments

(a)	The concentration of the bath gas Ar was varied over the range (2.7 - 120) x 1017 molecule cm-3. Some experiments with N2 were also conducted. Falloff extrapolations were made using Fc = 0.6.

(b)	Cl atoms were generated by photolysis of Cl2 in the presence of C2H2 and C2H6 (or C2H5Cl). The decays of C2H2, C2H6 (or C2H5Cl) were followed by FTIR spectroscopy. The measured rate coefficient ratios have been placed on an absolute basis using a rate coefficient of k(Cl + C2H6) = 5.7 x 10-11 cm3 molecule-1 s-1. Measurements were conducted over the pressure range 0.013 mbar to 7.6 bar. Falloff extrapolations were made with Fc = 0.6.

(c)	Mixtures of C2H2, C2H6, Cl2 and diluent (air, N2, or SF6) were irradiated by a UV fluorescent lamp. C2H2 and C2H6 concentrations were determined by GC. The reaction was studied at pressures between 0.03 bar and 1.7 bar. The measured rate coefficient ratios are placed on an absolute basis using the rate coefficient 8.68 x 10-11 exp(-113/T) cm3 molecule-1 s-1 for the reaction Cl + C2H6  C2H5 + HCl. Falloff extrapolations were made with a temperature independent Fc = 0.6.

(d)	Mixtures of Cl2, C2H2, CH4, CH3Cl, C2H6 and C2H5Cl and the diluent gases air and N2 were irradiated with a UV fluorescent lamp. After irradiation C2H2, CH4 and CH3Cl were monitored by GC (0.4 mbar to 13 mbar). CH3Cl, C2H6 and C2H5Cl were determined by FTIR (13 mbar to 920 mbar). The following values were used for the reference abstraction reactions: 1.0 x 10-13 cm3 molecule-1 s-1 (Cl + CH4), 4.9 x 10-13 cm3 molecule-1 s-1  (Cl + CH3Cl), 5.7 x 10-11 cm3 molecule-1 s-1 (Cl + C2H6) and 8.05 x 10-12 cm3 molecule-1 s-1 (Cl + C2H5Cl). The results were analyzed together with previous determinations performed between 0.13 bar and 7.9 bar and extrapolated with Fc = 0.6.2

Preferred Values

k0 = 6.1 x 10-30 (T/300)-3 [N2] cm3 molecule-1 s-1 over the temperature range 200 K to 300 K.

Reliability

log k0 = ± 0.3 at 298 K.

n = ± 1.

Comments on Preferred Values

The preferred values are based on the room temperature measurements of Kaiser and Wallington4 which have been evaluated with Fc = 0.6. The temperature dependence is a compromise of the results from refs. 1 and 3.

High-pressure rate coefficients

Rate coefficient data

| k/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/ Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| (1.52  0.15) x 10-4 T-2.63 | 210-361 | Brunning and Stief, 19851 | FP-RF (a) |
| 4.7 x 10-11 | 298 |  |  |
| Relative Rate Coefficients |  |  |  |
| 2.3 ± 0.7) x 10-10 | 295 | Wallington et al., 19902 | (b) |
| 2.13 x 10-10 (T/300)-1.045 | 252-370 | Kaiser, 19923 | (c) |
| (2.0 ± 0.1) x 10-10 | 297 | Kaiser and Wallington, 19964 | (d) |

Comments

(a) to (d)  See comments (a) to (d) for k0.

Preferred Values

k = 5.2 x 10-11 cm3 molecule-1 s-1 at 298 K and 1 bar of air.

k = 2.0 x 10-10 cm3 molecule-1 s-1, independent of temperature over the range 200 to 400 K.

Reliability

log k = ± 0.3 at 298 K.

n = ± 1.

Comments on Preferred Values

The preferred values are based on the data of Kaiser and Wallington4 which cover the broadest pressure range (0.13 bar to 7.9 bar). They have been evaluated with Fc = 0.6. Relative rate coefficients near 1 bar from refs. 5 to 7 are in good agreement with the preferred values. A branching ratio of 0.19  0.05 for formation of cis- and trans-isomers of the adduct in ref. 8 was determined around 1 bar of N2 and 295 K.

The following text-line combines the preferred values for the high and low pressure limiting rate coefficients to generate a single, cut-and-paste expression for calculation of k:

=((6.1e-30*(T/300)^-3)*M*(2.0e-10))/((6.1e-30*(T/300)^-3)*M+(2.0e-10))*10^(log10(0.6)/(1+(log10((6.1e-30*(T/300)^-3)*M/(2.0e-10))/(0.75-1.27*log10(0.6)))^2))

The molecular density, M = 7.2431021P(bar)/T(K)

References

- J. Brunning and L. J. Stief, J. Chem. Phys. 83, 1005 (1985).

- T. J. Wallington, J. M. Andino, I. M. Lorkovic, E. W. Kaiser, and G. Marston, J. Phys. Chem. 94, 3644 (1990).

- E. W. Kaiser, Int. J. Chem. Kinet. 24, 179 (1992).

- E. W. Kaiser and T. J. Wallington, J. Phys. Chem. 100, 4111 (1996).

- F. S. C. Lee and F. S. Rowland, J. Phys. Chem. 81, 684 (1977).

- R. Atkinson and S. M. Aschmann, Int. J. Chem. Kinet. 17, 33 (1985).

- T. J. Wallington, L. M. Skewes, and W. O. Siegl, J. Photochem. Photobiol. A45, 167 (1988).

- T. Zhu, G. Yarwood, J. Chen, and H. Niki, J. Phys. Chem. 98, 5065 (1994).