IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation – Data Sheet III.A2.50 iClOx35

Data sheets can be downloaded for personal use only and must not be re-transmitted or disseminated either electronically or in hard copy without explicit written permission. The citation for this data sheet is: IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation, (http://iupac.pole-ether.fr).

This data sheet last evaluated: March 2005.

ClO + ClO + M  Cl2O2 + M

H° = -75.7 kJ·mol-1

Low-pressure rate coefficients

Rate coefficient data

| k0/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| 5.0 x 10-32 [O2] | 298 | Johnston et al., 1969 | MM (a) |
| 2.0 x 10-32 [Ar] | 298 | Walker, 1972 | DF-UVA (b) |
| 1.1 x 10-32 [O2] | 300 | Basco and Hunt, 1979 | FP-UVA (c) |
| 3.0 x 10-32 [N2] | 298 | Cox et al., 1979 | MM (d) |
| 6.0 x 10-32 (T/300)-2.1 [O2] | 268-338 | Hayman et al., 1986 | MM (e) |
| (1.8 ± 0.5) x 10-32 (T/300)-3.6 [N2] | 194-247 | Sander, Friedl and Yung, 1989 | FP-UVA (f) |
| (1.64 ± 0.09) x 10-32 (T/300)-4.4 [N2] | 200-263 | Trolier, Mauldin and Ravishankara, 1990 | FP-UVA (g) |
| (1.32 ± 0.08) x 10-32 (T/300)-4.4 [O2] | 200-263 |  |  |
| 1.22 x 10-33 exp[(833 ± 34)/T] [N2] | 195-390 | Nickolaisen, Friedl and Sander, 1994 | FP-UVA (h) |
| (1.96 ± 0.24) x 10-32 [N2] | 300 |  |  |
| (1.24 ± 0.09) x 10-32 [O2] | 300 |  |  |
| (2.5 ± 0.4) x 10-32 [N2] | 300 | Bloss, 1999 | FP-UVA (i) |
| 1.7 x 10-32 [N2] | 300 | Stark, 1999 | PLP-UVA (j) |
| 1.1 x 10-31 [N2] | 200 |  |  |
| (1.59  0.60) x 10-32 (T/300)-4.5 [N2] | 183-245 | Bloss et al., 2001 | FP-UVA (k) |

# Comments

(a)	Photolysis of Cl2-O2 mixtures in the pressure range 0.07-1 bar.

(b)	Pressure range 1.3-10 mbar.

(c)	Pressure range 70-930 mbar.

(d)	Photolysis of Cl2-O2 mixtures at 50-400 mbar.

(e)	Measurements in Cl2-O2 mixtures in the ratio 2:3, pressure range 7-30 mbar.

(f)	ClO radicals generated from Cl2-Cl2O or Cl2-O3 mixtures with concentrations of bath gases N2, Ar or O2 in the range of 1018 molecule cm-3 to 3 x 1019 molecule cm-3.  Falloff extrapolations to k0 and k used a value of Fc = 0.6.

(g)	ClO radicals generated from Cl2-O3 mixtures in the presence of 33 mbar to 800 mbar of He, N2, O2 or SF6, ClO radicals and Cl2O2 monitored by long-path UV absorption.  Falloff curves extrapolated with Fc = 0.6.

(h)	Pulsed laser photolysis of Cl2 at  >300 nm in the presence of Cl2O.  ClO radicals generated by the reaction Cl + Cl2O  ClO + Cl2 and monitored by UV absorption spectroscopy using either a photomultiplier for detection at 275.5 nm or an optical multichannel analyzer for detection over the wavelength range 270 nm to 280 nm.  Measurements at 20-600 mbar. From a third-law analysis, a value of H° = -(75.7 ± 0.9) kJ mol-1 was derived.  Third-body efficiencies for the bath gases He, Ar, CF4, SF6 and Cl2 were also determined.

(i)	ClO radicals generated by flash photolysis of Cl2-Cl2O-N2 mixtures and detected by UV absorption.  The bath gas pressure was varied between 0.25 bar and 1 bar.  Falloff extrapolation used Fc = 0.6.  Small discrepancies between the various studies were attributed to the slightly different absorption cross-sections used.

(j)	ClO radicals generated by pulsed laser photolysis of Cl2O between 0.1 bar and 1000 bar pressure of He and N2.  The observed pressure dependences differ from conventional falloff expressions, suggesting overlapping contributions from the energy transfer and radical-complex mechanism, as well as diffusion control at the highest pressures.  The cited rate coefficients correspond to a representation of the falloff curve at pressures below 1 bar using Fc = 0.6.

(k)	See comment (i). Pressure range 30-930 mbar. Falloff extrapolation with Fc = 0.6 and k = (1.36  0.2) x 10-12 (T/300)-3.09 cm3 molecule-1 s-1.

# Preferred Values

k0 = 2.0 x 10-32(T/300)-4 [N2] cm-3 molecule-1 s-1 over the temperature range 190-300 K.

Reliability

log k0 = ± 0.1 at 298 K.

n = ± 1.5.

Comments on Preferred Values

The preferred values are based on the studies of Trolier et al. (1999) and Bloss et al. (2001) accounting for some falloff, see comments on high-pressure rate coefficients.

High-pressure rate coefficients

Rate coefficient data

| k/cm3 molecule-1 s-1 | Temp./K | Reference | Technique/Comments |
| --- | --- | --- | --- |
| Absolute Rate Coefficients |  |  |  |
| (6 ± 2) x 10-12 | 194-247 | Sander, Friedl and Yung, 1989 | FP-UVA (a) |
| (4.8 ± 1.3) x 10-12 | 200-263 | Trolier, Mauldin and Ravishankara, 1990 | FP-UVA (b) |
| (6 ± 2) x 10-12 | 195-390 | Nickolaisen, Friedl and Sander, 1994 | FP-UVA(c) |
| (5 ± 3) x 10-12 | 300 | Bloss, 1999 | FP-UVA (d) |
| 4.5 x 10-12 | 300 | Stark, 1999 | PLP-UVA (e) |
| 7 x 10-12 | 200 |  |  |
| (1.36  0.22) x 10-12 (T/300)-3.09 | 183-245 | Bloss et al., 2001 | FP-UVA (f) |

# Comments

(a)	See comment (a) for k0.

(b)	See comment (b) for k0.

(c)	See comment (c) for k0.  The k value was obtained from falloff data measured below 250 K.

(d)	See comment (d) for k0.

(e)	See comment (e) for k0.  The cited rate coefficients are given for the energy-transfer mechanism only, such that the falloff curves below 1 bar are fitted.  Above 1 bar pressure additional contributions from the radical-complex mechanism become increasingly important such that maximum values of k of 4.5 x 10-12 cm3 molecule-1 s-1 at 300 K and 8 x 10-12 cm3 molecule-1 s-1 at 200 K are reached near 200 bar, before they decrease because of diffusional control.

(f)	See comment (i) and (k) for k0.

# Preferred Values

k = 1.0 x 10-11 cm-3 molecule-1 s-1, independent of temperature over the range 190-300 K.

Reliability

log k = ± 0.3 over the temperature range 190 K to 300 K.

Comments on Preferred Values

It is difficult to provide a reasonable representation of k0, k, and Fc, because there is ample evidence that this reaction is governed by a superposition of the energy transfer and the radical-complex mechanism. The pressure dependence at P > 1 bar looks anomalous (Stark, 1999). Likewise, the absolute value and the temperature coefficient of k0 appear unusual. Neglecting these aspects, one may use the representation given by Bloss et al. (2001) with Fc = 0.6 and k0 and k as given in the table. We here choose a different representation with Fc = 0.45 and the preferred values given above which represent the data equally well at P < 1 bar. However, we keep in mind that the mechanistic complications of this system ask for different treatments. Difficulties in the theoretical analysis of the rate coefficients were also encountered by Bloss et al. (2001), Golden (2003) and Zhu and Lin (2003).

The following text-line combines the preferred values for the high and low pressure limiting rate coefficients to generate a single, cut-and-paste expression for calculation of  k:

=((2.0e-32*(T/300)^-4)*M*(1.0e-11))/((2.0e-32*(T/300)^-4)*M+(1.0e-11))*10^(log10(0.45)/(1+(log10((2.0e-32*(T/300)^-4)*M/(1.0e-11))/(0.75-1.27*log10(0.45)))^2))

The molecular density, M = 7.2431021P(bar)/T(K)

# References

Basco, N. and Hunt, J. K., Int. J. Chem. Kinet., 11, 649, 1979.

Bloss, W.: Ph.D. Thesis, University of Cambridge, Cambridge, UK, 1999.

Bloss, W. J., Nickolaisen, S. L., Salawitch, R. J., Friedl, R. R. and Sander, S. P.: J. Phys. Chem. A, 105, 11226, 2001.

Cox, R. A., Derwent, R. G., Eggleton, A. E. J. and Reid, H. J.: J. Chem. Soc. Faraday Trans. 1, 75, 1648, 1979.

Golden, D. M.: Int. J. Kinet., 35, 206, 2003.

Hayman, G. D., Davies, J. M. and Cox, R. A.: Geophys. Res. Lett., 13, 1347, 1986.

Johnston, H. S., Morris, E. D. and Van de Bogaerde, J.: J. Am. Chem. Soc. 91, 7712, 1969.

Nickolaisen, S. L., Friedl, R. R. and Sander, S. P.: J. Phys. Chem., 98, 155, 1994.

Sander, S. P., Friedl, R. R. and Yung, Y. L.: Science, 245, 1095, 1989.

Stark, H.: Ph.D. Thesis, University of Göttingen, Göttingen, Germany, 1999.

Trolier, M., Mauldin III, R. L. and Ravishankara, A. R.: J. Phys. Chem., 94, 4896, 1990.

Walker, R. W.: Ph.D. Thesis, University of London, London, UK, 1972.

Zhu, R. S. and Lin, M. C.: J. Chem. Phys., 118, 3094, 2003.